## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EX-ID-04 | Reduce the Wall Thickness of the Tailpipe from 1.2mm to 1mm. | Confirm cost savings | INR 84.0 | NG | Confirm cost savings | Kalp | 2024-04-15 00:00:00
2311-EX-ID-06 | Reduce the average wall thickness of the Exhaust Pipes (Pre-Silencer Outlet Pipe, Flexi Exhaust Outlet Connecting Pipe and Main Silencer Inlet Pipe) in MGI from 1.8mm and 1.4mm to 1.2mm as seen in KIA | nan | INR 60.0 | NG | nan | nan | nan
2311-EX-ID-02 | Replace the steel rods used in the fabrication of the exhaust hanger mounting brackets in MGI with hollow steel pipes as used in KIA | nan | INR 62.0 | NG | nan | nan | nan
2311-FS-ID-03 | Reduce the average wall thickness of the Baffle Plates present within the fuel tank assembly of MGI from 0.7mm to 0.6mm as seen in the fuel tank assembly of KIA | nan | INR 75.0 | NG | nan | nan | nan
2311-FS-ID-04 | Reduce the String Length of both the Fuel Inlet Steel Pipe and the Fuel Tank Vent Pipe 1. Reduce the string length of the Fuel Inlet Steel Pipe from 160mm to 120mm 2. Reduce the string length of the Fuel Tank Vent Pipe from 295mm to 110mm | nan | INR 93.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EX-ID-01 | 1. Remove the rubber hanger from the extension pipe near the resonator, along with its associated mounting points, and rearrange the other hangers as shown in the figure. 2. Relocate the hangers mounted on the resonator to the top and bottom of the resonator (onto the exhaust pipe and the extension pipe) | nan | INR 136.0 | NG | nan | nan | nan
2311-BIW-ID-05 | Reduce the Paint Coating Thickness of the highlighted Front Hood BiW Panel from 160 - 170μm to 100 - 110μm | nan | INR 82.0 | TBD | nan | nan | nan
2311-BIW-ID-07 | Reduce the Paint Coating Thickness of the highlighted Roof Side BiW Panels from 120 - 130μm to 100 - 110μm | nan | INR 71.0 | TBD | nan | nan | nan
2311-ET-ID-16 | Reduce the wall thickness of the Front Wheel Arch Liners present on both LH and RH sides from 1.6mm to 1.4mm | nan | INR 92.0 | NG | nan | nan | nan
2311-BIW-ID-03 | Reduce the Paint Coating Thicknesses of the highlighted Front Fender and Rear Quarter Panel BiW Panels from 120 - 130μm to 85 - 95μm | nan | INR 122.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-EX-ID-04 | 2311-EX-ID-06 | 2311-EX-ID-02 | 2311-FS-ID-03 | 2311-FS-ID-04 | 2311-EX-ID-01 | 2311-BIW-ID-05 | 2311-BIW-ID-07 | 2311-ET-ID-16 | 2311-BIW-ID-03
Savings (INR) | 84 | 60 | 62 | 75 | 93 | 136 | 82 | 71 | 92 | 122
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 3 | 7
• Total Ideas: 10
• Total Potential Savings: INR 877.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 3
• Status NG: 7
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 877.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI