## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-04 | Substitute the leather upholstery on the left-hand (LH) and right-hand (RH) sides of the third-row seat bases with the same fabric utilized on the LH and RH sides of the corresponding backrests | Check for combined business case | INR 48.0 | NG | Check for combined business case | Kalp | 2023-11-10 00:00:00
2311-PRODUCT-ID-11 | Reduce the width of the trunk liner flap by 60mm from the upper edge. | Confirm business case for 20mm reduction | INR 89.0 | TBD | Confirm business case for 20mm reduction | Kalp | 2024-02-14 00:00:00
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | Confirm on no part nuber change to avoid homologation cost | INR 115.0 | OK | Confirm on no part nuber change to avoid homologation cost | Nishant | 2024-06-17 00:00:00
2311-IT-ID-01 | Remove the fabric cover pasted onto the foot pad provided at the footwell area of the co-driver seat. | Check technical Feasibility | INR 52.0 | NG | Check technical Feasibility | Nishant | 2023-11-03 00:00:00
2311-DA-ID-27 | Replace ABS+PVC+PU with PP+PE-TD14 in the manufacture of both Front and Rear Passenger Armrest Trims of MGI | New tooling cost from YFI to be confirmed for business case calculations | INR 126.0 | NG | New tooling cost from YFI to be confirmed for business case calculations | Akhil | 2024-02-12 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Replace the current multi-density foam configuration in the seat cushions with a single-density, high-resilience foam, strategically sculpted to maintain ergonomic support and comfort profiles. | Investigate the acoustic and vibration damping properties of single-density foams versus multi-density configurations. Conduct Finite Element Analysis (FEA) to simulate load-bearing capacity and stress distribution under typical occupant weight. Perform subjective and objective comfort testing with representative user groups. Validate durability through accelerated aging and fatigue testing cycles, ensuring no compromise in tactile feel or long-term support. | 0 | AI Proposal | Investigate the acoustic and vibration damping properties of single-density foams versus multi-density configurations. Conduct Finite Element Analysis (FEA) to simulate load-bearing capacity and stress distribution under typical occupant weight. Perform subjective and objective comfort testing with representative user groups. Validate durability through accelerated aging and fatigue testing cycles, ensuring no compromise in tactile feel or long-term support. | VAVE | TBD
AI-GEN-02 | Eliminate the separate structural cross-member for the rear seat backrest frame and integrate its load-bearing function into the main seat chassis using a reinforced stamping process. | Perform stress analysis on the modified seat chassis to ensure it can withstand the bending and torsional loads typically handled by the removed cross-member. Evaluate the material thickness and geometry of the reinforced stamping for structural integrity. Conduct physical load testing on prototype seat frames to confirm performance against safety standards and dynamic load requirements. Analyze the tooling and manufacturing process changes required for the integrated design. | 0 | AI Proposal | Perform stress analysis on the modified seat chassis to ensure it can withstand the bending and torsional loads typically handled by the removed cross-member. Evaluate the material thickness and geometry of the reinforced stamping for structural integrity. Conduct physical load testing on prototype seat frames to confirm performance against safety standards and dynamic load requirements. Analyze the tooling and manufacturing process changes required for the integrated design. | VAVE | TBD
AI-GEN-03 | Substitute the current woven fabric seat cover with a knitted, engineered textile that offers comparable breathability, durability, and aesthetic qualities at a lower material cost and potentially reduced manufacturing complexity. | Source and evaluate knitted textiles for tensile strength, abrasion resistance, UV stability, and pilling characteristics. Conduct washability and colorfastness tests. Perform comfort evaluations for breathability and tactile feel. Assess the manufacturability of the knitted fabric onto the seat structure, including seam strength and drape. Validate fire retardancy to meet automotive standards. | 0 | AI Proposal | Source and evaluate knitted textiles for tensile strength, abrasion resistance, UV stability, and pilling characteristics. Conduct washability and colorfastness tests. Perform comfort evaluations for breathability and tactile feel. Assess the manufacturability of the knitted fabric onto the seat structure, including seam strength and drape. Validate fire retardancy to meet automotive standards. | VAVE | TBD
AI-GEN-04 | Reduce the number of stitching points and seam allowances in the seat upholstery by optimizing the pattern cutting and employing ultrasonic welding or adhesive bonding for certain fabric joints. | Analyze the structural integrity of seams under tension and shear forces. Perform pull-off tests for adhesive bonds and ultrasonic welds. Evaluate the long-term durability of these alternative joining methods against vibration and fatigue. Conduct aesthetic reviews to ensure a clean and high-quality finish. Validate that the reduced stitching does not compromise the fit or appearance of the upholstery. | 0 | AI Proposal | Analyze the structural integrity of seams under tension and shear forces. Perform pull-off tests for adhesive bonds and ultrasonic welds. Evaluate the long-term durability of these alternative joining methods against vibration and fatigue. Conduct aesthetic reviews to ensure a clean and high-quality finish. Validate that the reduced stitching does not compromise the fit or appearance of the upholstery. | VAVE | TBD
AI-GEN-05 | Replace the traditional spring-loaded recline mechanism with a simplified, friction-based locking system integrated directly into the seat frame components, requiring fewer parts and simpler assembly. | Design and prototype a friction-based locking mechanism that provides secure recline positioning across a range of occupant weights and vehicle dynamics. Analyze the frictional materials for wear resistance and long-term performance. Conduct extensive cycle testing to simulate repeated adjustments. Perform safety validation to ensure the mechanism holds position under acceleration, braking, and cornering forces. Evaluate user interface ergonomics for ease of adjustment. | 0 | AI Proposal | Design and prototype a friction-based locking mechanism that provides secure recline positioning across a range of occupant weights and vehicle dynamics. Analyze the frictional materials for wear resistance and long-term performance. Conduct extensive cycle testing to simulate repeated adjustments. Perform safety validation to ensure the mechanism holds position under acceleration, braking, and cornering forces. Evaluate user interface ergonomics for ease of adjustment. | VAVE | TBD
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-06 | De-content the internal seat frame padding by strategically contouring the primary seat foam to provide sufficient cushioning and impact absorption, thereby eliminating the need for a separate, thinner foam layer. | Utilize advanced foam molding techniques to create complex contours in the primary seat foam that mimic the protective and supportive functions of the removed padding. Conduct impact absorption simulations using anthropomorphic test devices (ATDs) to verify energy dissipation. Perform comfort evaluations to ensure no pressure points or discomfort arise from the direct foam-to-trim interface. Validate that the structural integrity of the seat frame is not compromised by the change in internal support. | 0 | AI Proposal | Utilize advanced foam molding techniques to create complex contours in the primary seat foam that mimic the protective and supportive functions of the removed padding. Conduct impact absorption simulations using anthropomorphic test devices (ATDs) to verify energy dissipation. Perform comfort evaluations to ensure no pressure points or discomfort arise from the direct foam-to-trim interface. Validate that the structural integrity of the seat frame is not compromised by the change in internal support. | VAVE | TBD
WEB-GEN-01 | Streamline Design and Technical Team Collaboration for Efficiency | Implement cross-functional workshops and integrated project management tools to improve communication and reduce duplicated efforts between design and technical teams. This can lead to faster problem-solving and fewer design iterations. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | 0 | Web Sourced | Implement cross-functional workshops and integrated project management tools to improve communication and reduce duplicated efforts between design and technical teams. This can lead to faster problem-solving and fewer design iterations. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | VAVE | TBD
WEB-GEN-02 | Prioritize Development Resources Based on Performance Gains | Establish a rigorous analysis framework to quantify the performance benefit (e.g., 'tenths per month') of ongoing development projects. Allocate R&D budget and engineering hours to initiatives offering the highest return in performance, ensuring efficient use of resources. Source: https://www.f1technical.net/forum/viewtopic.php?t=32051&start=7200 | 0 | Web Sourced | Establish a rigorous analysis framework to quantify the performance benefit (e.g., 'tenths per month') of ongoing development projects. Allocate R&D budget and engineering hours to initiatives offering the highest return in performance, ensuring efficient use of resources. Source: https://www.f1technical.net/forum/viewtopic.php?t=32051&start=7200 | VAVE | TBD
Generated by VAVE-AI

## Slide 5: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-SS-ID-04 | 2311-PRODUCT-ID-11 | 2311-PRODUCT-ID-07 | 2311-IT-ID-01 | 2311-DA-ID-27 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03 | AI-GEN-04 | AI-GEN-05 | AI-GEN-06 | WEB-GEN-01 | WEB-GEN-02
Savings (INR) | 48 | 89 | 115 | 52 | 126 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 6: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 1 | 1 | 3
• Total Ideas: 13
• Total Potential Savings: INR 430.00
• Implemented Ideas: 0
• Status OK: 1
• Status TBD: 1
• Status NG: 3
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 7: Summary section
Total Ideas: 13 ideas analyzed.
Total Savings: INR 430.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI