## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-04 | Substitute the leather upholstery on the left-hand (LH) and right-hand (RH) sides of the third-row seat bases with the same fabric utilized on the LH and RH sides of the corresponding backrests | Check for combined business case | INR 48.0 | NG | Check for combined business case | Kalp | 2023-11-10 00:00:00
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | Confirm on no part nuber change to avoid homologation cost | INR 115.0 | OK | Confirm on no part nuber change to avoid homologation cost | Nishant | 2024-06-17 00:00:00
2311-PRODUCT-ID-13 | Eliminate the plastic trim provided around the bottom anchor point at the driver side seatbelt and follow the same methodology provided at the co-driver's side. | None | INR 141.0 | NG | None | None | None
2311-PRODUCT-ID-09 | De-content the Plastic Protective Trims fitted onto the LHS and RHS mounting points of the third-row seats and cover the same with the fabric used on the vehicle floor. | Confirm on PTR plan | INR 76.0 | OK | Confirm on PTR plan | Harsh | 2024-06-14 00:00:00
2311-IT-ID-05 | Replace the TPE Coaster/Insert positioned at the base of the front centre armrest storage compartment with a Fabric one | None | INR 40.0 | NG | None | None | None
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-02 | 1. Reduce the width of the seat adjustment lever-2 from 345mm to 175mm commonising both. 2. Reduce the overall diameter of the bars from 13mm to 12mm. | Check for combined business case | INR 74.0 | NG | Check for combined business case | Kalp | 2023-11-07 00:00:00
2311-SS-ID-05 | 1. Replace the leather upholstery on the flaps located at the bottom of MGI's front-row seats with fabric 2. Use the same fabric (polyester) used to upholster the unexposed seat sides within MGI | one-pager for PP approval | INR 113.0 | NG | one-pager for PP approval | Ratnadeep | 2023-11-20 00:00:00
2311-PRODUCT-ID-10 | Reduce the length of the Seat Release Straps found on the second and third-row seats | None | INR 86.0 | NG | None | None | None
2311-SS-ID-11 | Process Deletion, Remove the Black Painting done on the Driver and Co-Driver Seat Base Support Frames | None | INR 90.0 | NG | None | None | None
2311-SS-ID-10 | Replace PP+EPDM-T20 used in the manufacture of the Second-Row Seat Bottom Cover and Cushion Cover Trims of MGI with standard PP | All trims foam & cover idea will be again checked for feasibility with supplier & BC evaluation. | INR 147.0 | NG | All trims foam & cover idea will be again checked for feasibility with supplier & BC evaluation. | Kalp/Nishant | 2023-12-31 00:00:00
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-SS-ID-04 | 2311-PRODUCT-ID-07 | 2311-PRODUCT-ID-13 | 2311-PRODUCT-ID-09 | 2311-IT-ID-05 | 2311-SS-ID-02 | 2311-SS-ID-05 | 2311-PRODUCT-ID-10 | 2311-SS-ID-11 | 2311-SS-ID-10
Savings (INR) | 48 | 115 | 141 | 76 | 40 | 74 | 113 | 86 | 90 | 147
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 2 | 0 | 8
• Total Ideas: 10
• Total Potential Savings: INR 930.00
• Implemented Ideas: 0
• Status OK: 2
• Status TBD: 0
• Status NG: 8
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 930.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI