## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-03 | Remove the Air Extractor Vent Securing Trims affixed at both ends of the rear bumper brackets of the vehicle | nan | INR 148.0 | NG | nan | nan | nan
2311-DA-ID-06 | Replace the plastic trim used on the Hood Prop Rod in MGI with a foam cover trim as in KIA | Check supplier feasibility | INR 148.0 | NG | Check supplier feasibility | Chirag | 2024-02-16 00:00:00
2311-DA-ID-22 | Replace PA6-GF30 with PA6-GF15 + MD25 in the manufacture of the Exterior Door Handle Rear Trims | nan | INR 148.0 | NG | nan | nan | nan
2311-DA-ID-26 | Replace the ABS blend with PP-T20 in the manufacture of the Front and Rear Door Panel Side Trims in MGI | nan | INR 147.0 | NG | nan | nan | nan
2311-SS-ID-10 | Replace PP+EPDM-T20 used in the manufacture of the Second-Row Seat Bottom Cover and Cushion Cover Trims of MGI with standard PP | All trims foam & cover idea will be again checked for feasibility with supplier & BC evaluation. | INR 147.0 | NG | All trims foam & cover idea will be again checked for feasibility with supplier & BC evaluation. | Kalp/Nishant | 2023-12-31 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-35 | Replace PBT-GF30 with PA6-GF30 in the manufacture of the gear casings. | Consider in homeroom bucket | INR 147.0 | Hold | Consider in homeroom bucket | Ratnadeep | TBC
2311-IT-ID-26 | Replace PP-T20 with PP in the manufacture of the grab handles within the vehicle | nan | INR 145.0 | TBD | nan | nan | nan
2311-IT-ID-16 | Replace PP+PE-T10 used in the manufacture of the Front A-Pillar Interior Trims in MGI with standard PP+PE | nan | INR 145.0 | NG | nan | nan | nan
2311-ET-ID-27 | Replace the Thinsulate Acoustic Insulation used on the Front & Rear Wheel Arch LH & RH Liners for NVH restriction within MGI with Noiselite PP-PET Insulation | nan | INR 145.0 | TBD | nan | nan | nan
2311-IT-ID-06 | Eliminate the dead pedal trim provided in MGI. | Confirm date for sample availability (Functional & Appearance check) - 1Nos 6 seater carpet without cut-out for dead pedal | INR 144.0 | OK | Confirm date for sample availability (Functional & Appearance check) - 1Nos 6 seater carpet without cut-out for dead pedal | Akhil | 2024-06-15 00:00:00
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-FS-ID-02 | Replace the Steel access cover used within MGI with a Plastic (PP(assumed)) one as used in KIA | Confirm technical feasibilty | INR 144.0 | TBD | Confirm technical feasibilty | Sumanta | 2024-04-23 00:00:00
2311-SS-ID-01 | Reduce the width from the upper edge of the PVC panel of seat vent by 90mm. | nan | INR 144.0 | NG | nan | nan | nan
2311-DA-ID-07 | Replace PA6-GF30 with PA6-GF20 in the manufacture of the Tailgate Release/Handle Trim | Confirm change content | INR 143.0 | NG | Confirm change content | Narendra | 2023-11-24 00:00:00
2311-EL-ID-01 | Replace the 16-pin connector set used on the IRVM assembly with an 8-pin connector set. | Confirm on 10 pin connector availability with supplier (similar to Kia) | INR 142.0 | NG | Confirm on 10 pin connector availability with supplier (similar to Kia) | Narendra | 2023-11-24 00:00:00
2311-FS-ID-01 | Remove the Neoprene Foam Sheaths present on the fuel lines and the fuel inlet hose of MGI | Confirm Kia routing photos for analysis with ASI | INR 142.0 | NG | Confirm Kia routing photos for analysis with ASI | Ratnadeep | 2024-02-12 00:00:00
Generated by VAVE-AI

## Slide 5
Ideas Summary (Part 4)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IP-ID-05 | Replace PP+EPDM+T20 with PP+T20 in the manufacture of the dashboard upper trim of the vehicle | nan | INR 141.0 | NG | nan | nan | nan
2311-PRODUCT-ID-13 | Eliminate the plastic trim provided around the bottom anchor point at the driver side seatbelt and follow the same methodology provided at the co-driver's side. | nan | INR 141.0 | NG | nan | nan | nan
2311-PRODUCT-ID-18 | Reduce the diameter of the Headrest Rods from 12.6mm to 10mm | Check for combined business case | INR 141.0 | NG | Check for combined business case | Kalp | 2023-11-24 00:00:00
2311-ET-ID-17 | Reduce the wall thickness of the Bumper Lower Trim from 2.8mm to 2.4mm | nan | INR 141.0 | NG | nan | nan | nan
2311-IP-ID-16 | Replace PC-ABS with ABS in the manufacture of both Instrument Cluster Fascia Decorative Trim and the IP LHS & RHS Decorative Trims since the finish could be achieved on ABS-made trims as well | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 140.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
Generated by VAVE-AI

## Slide 6
Ideas Summary (Part 5)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IT-ID-17 | Replace the Thinsulate used in between the Interior Trims of MGI with Felt | Confirm on part availability | INR 140.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
2311-EL-ID-25 | Replace Brass with Steel in the manufacture of the Main Terminal Connector Bolt within the Engine-Bay Fusebox Assembly of MGI | nan | INR 140.0 | TBD | nan | nan | nan
2311-EL-ID-17 | Replace the oxygen sensors used in MGI with the oxygen sensors used in KIA | Homeroom ideas to be bunched up and taken up for implementation at program level | INR 139.0 | Hold | Homeroom ideas to be bunched up and taken up for implementation at program level | Manish Jaju | 2024-02-20 00:00:00
2311-IP-ID-11 | Replace PC-ABS with PP-TD40 in the manufacture of the Front-Row Air Vent Casings in MGI | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 138.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-EL-ID-11 | Replace PC-ABS with ABS in the manufacture of Tail Lamp Housings of MGI | nan | INR 137.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 7
Ideas Summary (Part 6)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IT-ID-08 | Remove the EPDM sheet and integrate the PU Foam with the PE sheet. | Confirm on vehicel trial | INR 137.0 | OK | Confirm on vehicel trial | Narendra/ Ratnadeep | 2024-06-28 00:00:00
2311-EX-ID-01 | 1. Remove the rubber hanger from the extension pipe near the resonator, along with its associated mounting points, and rearrange the other hangers as shown in the figure. 2. Relocate the hangers mounted on the resonator to the top and bottom of the resonator (onto the exhaust pipe and the extension pipe) | nan | INR 136.0 | NG | nan | nan | nan
2311-EL-ID-08 | Update the battery mounting technique in MGI to align with the one employed in KIA, including a redesign of the battery-securing enclosure. | nan | INR 135.0 | TBD | nan | nan | nan
2311-DA-ID-10 | Instead of using Aluminum in the manufacture of the Mirror Main Frame, use PA6-GF 50 | Homeroom ideas to be bunched up and taken up for new program | INR 135.0 | NG | Homeroom ideas to be bunched up and taken up for new program | nan | nan
2311-PRODUCT-ID-05 | Reduce the projection of the 'HECTOR' badging on the tailgate at the rear end of the car from 4mm to 2.5mm | Verify business case | INR 135.0 | NG | Verify business case | Kalp | 2023-11-24 00:00:00
Generated by VAVE-AI

## Slide 8
Ideas Summary (Part 7)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-BIW-ID-06 | Reduce the Paint Coating Thickness of the highlighted Roof BiW Panel from 110 - 120μm to 70 - 80μm | nan | INR 135.0 | TBD | nan | nan | nan
2311-DA-ID-25 | Replace PP-T20 used in the manufacture of the Door Panel Interior Main Trims 2 of MGI with PP-E/P-TD10 | Business case to be evaluated (combined for DA-ID-24 & 25) | INR 134.0 | NG | Business case to be evaluated (combined for DA-ID-24 & 25) | Kalp | 2023-11-24 00:00:00
2311-ET-ID-20 | Replace the PCB Module supplied by 'Taizhou Suzhong Antenna Group Co., Ltd.' used within the shark fin antenna of MGI with a similar one supplied by 'INFAC Elecs' used in KIA | nan | INR 133.0 | TBD | nan | nan | nan
2311-ET-ID-07 | Reduce the wall thickness of the Front and Rear Fender Garnishes present on both LH and RH sides from 3.2mm to 2.8mm | nan | INR 133.0 | NG | nan | nan | nan
2311-ET-ID-24 | Redesign the current front logo assembly making the mentioned changes, 1. Remove the Logo Holder (Black) 2. Instead of chrome plating the Logo Holding Bracket, finish it in Black and snap-fit the logo M and G onto this 3. Introduce a new chrome-plated edge trim to complete the design | nan | INR 132.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 9
Ideas Summary (Part 8)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-12 | Replace ABS with PP-GF 15 in the manufacture of the LH and RH Side Spoiler Inner Trims | nan | INR 131.0 | NG | nan | nan | nan
2311-ET-ID-11 | 1. Remove the Foam inserts from both the LH and RH sides of MGI and use plastic trims instead as employed in KIA 2. Thinsulate could be used if required | nan | INR 131.0 | NG | nan | nan | nan
2311-IP-ID-01 | Replace the Thinsulate used within the LH & RH Centre Console Side Trims of MGI with Thermoplastic Felt | Confirm on part availability | INR 131.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
2311-ST-ID-03 | Replace the Cast Aluminium Steering Column Mount in MGI with a fabricated sheet welded onto the shaft as used in KIA | nan | INR 131.0 | NG | nan | nan | nan
2311-IP-ID-10 | Replace PC-ABS with ABS in the manufacture of the Front-Row Armrest Inner Cover in MGI | nan | INR 130.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 10
Ideas Summary (Part 9)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-WT-ID-01 | Replace the Tyre Pressure Monitoring System (TPMS) sensors from 'SGMW' used in MGI with similar sensors from 'Continental Engineering Services' used in KIA. | nan | INR 130.0 | TBD | nan | nan | nan
2311-BIW-ID-02 | Remove the black paint coating from the LH & RH A-Pillar Side Stiffener Brackets, LH & RH Centre Console and Gear Selector Base Mounting Brackets on the BIW of MGI | CFT buy off | INR 130.0 | TBD | CFT buy off | Ratnadeep | 2024-03-29 00:00:00
2311-PRODUCT-ID-02 | Replace the Plastic Caps mounted onto the doors, hood, and tailgate (total 14) with adhesive stickers. | nan | INR 130.0 | NG | nan | nan | nan
2311-DA-ID-18 | Replace ABS with PP-T 20 in the manufacture of Door Panel Interior Delta Trim Inners | Check Bussiness case | INR 129.0 | NG | Check Bussiness case | Kalp | 2023-11-08 00:00:00
2311-DA-ID-20 | De-content Cable Protective Sheaths one each from all the Lock Release and Front Window Regulator assemblies of the vehicle | Confirm homeroom feasibilty | INR 129.0 | NG | Confirm homeroom feasibilty | Manish | TBD
Generated by VAVE-AI

## Slide 11
Ideas Summary (Part 10)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-37 | Replace ABS with PP-T20 used in the manufacture of the LH and RH Mirror Outer Covers of MGI | nan | INR 127.0 | TBD | nan | nan | nan
2311-EL-ID-23 | Replace the Mini (Closed) Fuses used within the Engine-Bay Fuse Box of the vehicle with Micro2 (Open) Fuses | nan | INR 127.0 | TBD | nan | nan | nan
2311-SP-ID-03 | Redesign the rubber mould removing the 16mm extension downwards from all three sides of the plate | nan | INR 127.0 | NG | nan | nan | nan
2311-DA-ID-27 | Replace ABS+PVC+PU with PP+PE-TD14 in the manufacture of both Front and Rear Passenger Armrest Trims of MGI | New tooling cost from YFI to be confirmed for business case calculations | INR 126.0 | NG | New tooling cost from YFI to be confirmed for business case calculations | Akhil | 2024-02-12 00:00:00
2311-PRODUCT-ID-03 | Replace the rubber bushes used on the wiper blade mounting bolts with the plastic protective cap. | nan | INR 126.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 12
Ideas Summary (Part 11)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Transition from stamped steel to a forged aluminum alloy (e.g., 6061-T6) for the front lower control arms. | Forging aluminum alloys allows for complex geometries and grain flow optimization, leading to superior strength-to-weight ratios compared to stamped steel. This reduces unsprung mass, improving dynamic response and ride comfort. Validation will involve FEA simulations to verify structural integrity under critical load cases (braking, cornering, impact), followed by physical testing of prototypes using a shaker rig and a proving ground for real-world performance assessment. | 0 | AI Proposal | Forging aluminum alloys allows for complex geometries and grain flow optimization, leading to superior strength-to-weight ratios compared to stamped steel. This reduces unsprung mass, improving dynamic response and ride comfort. Validation will involve FEA simulations to verify structural integrity under critical load cases (braking, cornering, impact), followed by physical testing of prototypes using a shaker rig and a proving ground for real-world performance assessment. | VAVE | TBD
AI-GEN-02 | Utilize a high-strength aluminum casting (e.g., A356-T6) for the front lower control arms, incorporating hollow sections and optimized ribbing. | Casting offers significant design freedom, enabling the integration of features like internal voids and strategic reinforcement. This minimizes material usage while maintaining necessary stiffness and durability. The manufacturing process can be more cost-effective than forging for certain complex shapes. Validation will include extensive CAE analysis for stress and fatigue life prediction, followed by destructive testing (e.g., tensile, fatigue) and dynamic vehicle testing on a controlled track. | 0 | AI Proposal | Casting offers significant design freedom, enabling the integration of features like internal voids and strategic reinforcement. This minimizes material usage while maintaining necessary stiffness and durability. The manufacturing process can be more cost-effective than forging for certain complex shapes. Validation will include extensive CAE analysis for stress and fatigue life prediction, followed by destructive testing (e.g., tensile, fatigue) and dynamic vehicle testing on a controlled track. | VAVE | TBD
AI-GEN-03 | Employ a fiber-reinforced polymer (FRP) composite, such as carbon fiber or glass fiber with a high-performance resin matrix, for the front lower control arms. | Composites offer exceptional stiffness and strength at a fraction of the weight of steel or even aluminum. Advanced lay-up techniques can tailor material properties to specific load requirements, further optimizing performance. This approach significantly reduces unsprung mass, enhancing agility and fuel efficiency. Validation will focus on fatigue and impact resistance testing using specialized composite testing equipment, alongside rigorous vehicle dynamics testing to quantify performance gains. | 0 | AI Proposal | Composites offer exceptional stiffness and strength at a fraction of the weight of steel or even aluminum. Advanced lay-up techniques can tailor material properties to specific load requirements, further optimizing performance. This approach significantly reduces unsprung mass, enhancing agility and fuel efficiency. Validation will focus on fatigue and impact resistance testing using specialized composite testing equipment, alongside rigorous vehicle dynamics testing to quantify performance gains. | VAVE | TBD
AI-GEN-04 | Develop a hybrid aluminum-composite structure for the front lower control arms, where critical stress areas utilize forged aluminum inserts integrated within a composite shell. | This approach leverages the strengths of both materials. Aluminum provides excellent localized strength and impact resistance at mounting points and high-stress zones, while the composite offers low weight and high stiffness for the bulk of the arm. This provides a balance of performance, durability, and weight savings. Validation will involve detailed multi-material FEA, followed by component-level testing of the bonded interfaces and full vehicle testing to assess dynamic behavior and durability. | 0 | AI Proposal | This approach leverages the strengths of both materials. Aluminum provides excellent localized strength and impact resistance at mounting points and high-stress zones, while the composite offers low weight and high stiffness for the bulk of the arm. This provides a balance of performance, durability, and weight savings. Validation will involve detailed multi-material FEA, followed by component-level testing of the bonded interfaces and full vehicle testing to assess dynamic behavior and durability. | VAVE | TBD
AI-GEN-05 | Investigate advanced high-strength steel (AHSS) with optimized stamping and hydroforming techniques for the front lower control arms to reduce material thickness and optimize section modulus. | While not an alternative material in terms of composition, AHSS allows for significantly thinner gauges and more complex shapes than traditional stamped steel. Hydroforming can create hollow sections and intricate profiles, achieving weight savings and improved stiffness. This offers a more evolutionary approach to mass reduction within existing steel supply chains. Validation will involve detailed stamping simulations, hydroforming process modeling, and extensive static and dynamic testing of the optimized AHSS components. | 0 | AI Proposal | While not an alternative material in terms of composition, AHSS allows for significantly thinner gauges and more complex shapes than traditional stamped steel. Hydroforming can create hollow sections and intricate profiles, achieving weight savings and improved stiffness. This offers a more evolutionary approach to mass reduction within existing steel supply chains. Validation will involve detailed stamping simulations, hydroforming process modeling, and extensive static and dynamic testing of the optimized AHSS components. | VAVE | TBD
Generated by VAVE-AI

## Slide 13
Ideas Summary (Part 12)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-06 | Explore the use of magnesium alloys (e.g., AZ91D) for the front lower control arms, potentially through die casting or thixotropic forming. | Magnesium alloys offer a density significantly lower than aluminum, providing the greatest potential for unsprung mass reduction. Die casting allows for high-volume production of complex shapes. While challenges exist in corrosion resistance and impact toughness, advancements in alloy development and coating technologies are mitigating these concerns. Validation will focus on material characterization, corrosion testing, impact simulations, and comprehensive vehicle testing to ensure long-term durability and performance. | 0 | AI Proposal | Magnesium alloys offer a density significantly lower than aluminum, providing the greatest potential for unsprung mass reduction. Die casting allows for high-volume production of complex shapes. While challenges exist in corrosion resistance and impact toughness, advancements in alloy development and coating technologies are mitigating these concerns. Validation will focus on material characterization, corrosion testing, impact simulations, and comprehensive vehicle testing to ensure long-term durability and performance. | VAVE | TBD
Generated by VAVE-AI

## Slide 14: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-ET-ID-03 | 2311-DA-ID-06 | 2311-DA-ID-22 | 2311-DA-ID-26 | 2311-SS-ID-10 | 2311-DA-ID-35 | 2311-IT-ID-26 | 2311-IT-ID-16 | 2311-ET-ID-27 | 2311-IT-ID-06 | 2311-FS-ID-02 | 2311-SS-ID-01 | 2311-DA-ID-07 | 2311-EL-ID-01 | 2311-FS-ID-01 | 2311-IP-ID-05 | 2311-PRODUCT-ID-13 | 2311-PRODUCT-ID-18 | 2311-ET-ID-17 | 2311-IP-ID-16 | 2311-IT-ID-17 | 2311-EL-ID-25 | 2311-EL-ID-17 | 2311-IP-ID-11 | 2311-EL-ID-11 | 2311-IT-ID-08 | 2311-EX-ID-01 | 2311-EL-ID-08 | 2311-DA-ID-10 | 2311-PRODUCT-ID-05 | 2311-BIW-ID-06 | 2311-DA-ID-25 | 2311-ET-ID-20 | 2311-ET-ID-07 | 2311-ET-ID-24 | 2311-DA-ID-12 | 2311-ET-ID-11 | 2311-IP-ID-01 | 2311-ST-ID-03 | 2311-IP-ID-10 | 2311-WT-ID-01 | 2311-BIW-ID-02 | 2311-PRODUCT-ID-02 | 2311-DA-ID-18 | 2311-DA-ID-20 | 2311-DA-ID-37 | 2311-EL-ID-23 | 2311-SP-ID-03 | 2311-DA-ID-27 | 2311-PRODUCT-ID-03 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03 | AI-GEN-04 | AI-GEN-05 | AI-GEN-06
Savings (INR) | 148 | 148 | 148 | 147 | 147 | 147 | 145 | 145 | 145 | 144 | 144 | 144 | 143 | 142 | 142 | 141 | 141 | 141 | 141 | 140 | 140 | 140 | 139 | 138 | 137 | 137 | 136 | 135 | 135 | 135 | 135 | 134 | 133 | 133 | 132 | 131 | 131 | 131 | 131 | 130 | 130 | 130 | 130 | 129 | 129 | 127 | 127 | 127 | 126 | 126 | 0 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 15: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 2 | 16 | 30
• Total Ideas: 56
• Total Potential Savings: INR 6,857.00
• Implemented Ideas: 0
• Status OK: 2
• Status TBD: 16
• Status NG: 30
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 16: Summary section
Total Ideas: 56 ideas analyzed.
Total Savings: INR 6,857.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI