## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
VAVE-SWI-046 | Cluster Bezel Ring Platin to Painting | nan | INR 0.0 | NG | nan | nan | nan
2311-IT-ID-05 | Replace the TPE Coaster/Insert positioned at the base of the front centre armrest storage compartment with a Fabric one | nan | INR 40.0 | NG | nan | nan | nan
2311-EL-ID-01 | Replace the 16-pin connector set used on the IRVM assembly with an 8-pin connector set. | Confirm on 10 pin connector availability with supplier (similar to Kia) | INR 142.0 | NG | Confirm on 10 pin connector availability with supplier (similar to Kia) | Narendra | 2023-11-24 00:00:00
2311-IP-ID-16 | Replace PC-ABS with ABS in the manufacture of both Instrument Cluster Fascia Decorative Trim and the IP LHS & RHS Decorative Trims since the finish could be achieved on ABS-made trims as well | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 140.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-EC-ID-02 | Route the Radiator to the Oil Chiller Hose through the right side of the Radiator to the Engine Assembly Hose as shown in the diagrams, resulting in a 100mm reduction in the overall hose length. | nan | INR 57.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IP-ID-15 | Replace PC-ABS with ABS in the manufacture of IP LHS & RHS Trims since the finish could be achieved on ABS-made trims as well | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 60.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-PRODUCT-ID-03 | Replace the rubber bushes used on the wiper blade mounting bolts with the plastic protective cap. | nan | INR 126.0 | NG | nan | nan | nan
VAVE-SWI-035 | Mirror button material change SS-USA To ZAMAK 5 -Local | nan | INR 8.0 | NG | nan | nan | nan
VAVE-SWI-004 | Suspension - Dust cap weight reduction | nan | INR 0.0 | NG | nan | nan | nan
2311-IP-ID-14 | Redesign the Instrument Cluster Fascia separating both the garnish trim and the fascia while simultaneously replacing PC-ABS with PP-TD20 in the manufacture of the separated fascia | nan | INR 111.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| VAVE-SWI-046 | 2311-IT-ID-05 | 2311-EL-ID-01 | 2311-IP-ID-16 | 2311-EC-ID-02 | 2311-IP-ID-15 | 2311-PRODUCT-ID-03 | VAVE-SWI-035 | VAVE-SWI-004 | 2311-IP-ID-14
Savings (INR) | 0 | 40 | 142 | 140 | 57 | 60 | 126 | 8 | 0 | 111
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 2 | 8
• Total Ideas: 10
• Total Potential Savings: INR 684.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 2
• Status NG: 8
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 684.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI