## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-24 | Redesign the current front logo assembly making the mentioned changes, 1. Remove the Logo Holder (Black) 2. Instead of chrome plating the Logo Holding Bracket, finish it in Black and snap-fit the logo M and G onto this 3. Introduce a new chrome-plated edge trim to complete the design | nan | INR 132.0 | TBD | nan | nan | nan
2311-DA-ID-27 | Replace ABS+PVC+PU with PP+PE-TD14 in the manufacture of both Front and Rear Passenger Armrest Trims of MGI | New tooling cost from YFI to be confirmed for business case calculations | INR 126.0 | NG | New tooling cost from YFI to be confirmed for business case calculations | Akhil | 2024-02-12 00:00:00
2311-DA-ID-02 | Substitute ABS with PP-T20 for the production of the Door Recess Trims fastened onto the door control panel trims | Confirm on part availabilty and trial | INR 55.0 | NG | Confirm on part availabilty and trial | Akhil/ Narendra | 2024-02-16 00:00:00
2311-IP-ID-10 | Replace PC-ABS with ABS in the manufacture of the Front-Row Armrest Inner Cover in MGI | nan | INR 130.0 | NG | nan | nan | nan
2311-IP-ID-03 | Replace PC-ABS with ABS in the manufacture of Centre Console LH and RH Garnish Trims and the Infotainment Screen Garnish Trim present within the interior of the vehicle | Supplier evalutiaon | INR 72.0 | NG | Supplier evalutiaon | Narendra | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-AI-ID-04 | Redesign the Air Intake Upper Trim removing the service cover and the provisions provided to snap fit the same | nan | INR 42.0 | NG | nan | nan | nan
2311-DA-ID-10 | Instead of using Aluminum in the manufacture of the Mirror Main Frame, use PA6-GF 50 | Homeroom ideas to be bunched up and taken up for new program | INR 135.0 | NG | Homeroom ideas to be bunched up and taken up for new program | nan | nan
2311-DA-ID-03 | Replace PA6-G30 with PA6-GF20 in the manufacture of Speaker/Door Handle Housing Trim | Confirm business case | INR 66.0 | NG | Confirm business case | Kalp | 2023-11-02 00:00:00
2311-IP-ID-06 | Replace PC-ABS with ABS in the manufacture of the Front-Row Armrest Base in MGI | nan | INR 126.0 | NG | nan | nan | nan
2311-SS-ID-08 | Replace PP-T20 and PP+EPDM-T20 with standard PP in the manufacture of Front-Row Seating Assembly Side Cover Trims | nan | INR 119.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-ET-ID-24 | 2311-DA-ID-27 | 2311-DA-ID-02 | 2311-IP-ID-10 | 2311-IP-ID-03 | 2311-AI-ID-04 | 2311-DA-ID-10 | 2311-DA-ID-03 | 2311-IP-ID-06 | 2311-SS-ID-08
Savings (INR) | 132 | 126 | 55 | 130 | 72 | 42 | 135 | 66 | 126 | 119
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 1 | 9
• Total Ideas: 10
• Total Potential Savings: INR 1,003.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 1
• Status NG: 9
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 1,003.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI