## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-24 | Redesign the current front logo assembly making the mentioned changes, 1. Remove the Logo Holder (Black) 2. Instead of chrome plating the Logo Holding Bracket, finish it in Black and snap-fit the logo M and G onto this 3. Introduce a new chrome-plated edge trim to complete the design | nan | INR 132.0 | TBD | nan | nan | nan
2311-IT-ID-22 | Replace PP-T20 used in the manufacture of the Third Row LH & RH Cup Holders with PP | nan | INR 42.0 | TBD | nan | nan | nan
2311-IP-ID-04 | Replace ABS with PP-T20 in the manufacture of the Front-Row Handrest Rear Trim | nan | INR 87.0 | NG | nan | nan | nan
2311-SS-ID-04 | Substitute the leather upholstery on the left-hand (LH) and right-hand (RH) sides of the third-row seat bases with the same fabric utilized on the LH and RH sides of the corresponding backrests | Check for combined business case | INR 48.0 | NG | Check for combined business case | Kalp | 2023-11-10 00:00:00
2311-IP-ID-15 | Replace PC-ABS with ABS in the manufacture of IP LHS & RHS Trims since the finish could be achieved on ABS-made trims as well | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 60.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IP-ID-02 | Replace PC+ABS/TPU used in the manufacture of the Centre Console Bottle Holder Trim with PP | Supplier evalutiaon | INR 87.0 | TBD | Supplier evalutiaon | Narendra | 2024-02-22 00:00:00
2311-EL-ID-17 | Replace the oxygen sensors used in MGI with the oxygen sensors used in KIA | Homeroom ideas to be bunched up and taken up for implementation at program level | INR 139.0 | Hold | Homeroom ideas to be bunched up and taken up for implementation at program level | Manish Jaju | 2024-02-20 00:00:00
2311-DA-ID-34 | Replace the Door Lock Request Sensor Assemblies used in MGI with the one used in KIA | nan | INR 100.0 | TBD | nan | nan | nan
2311-DA-ID-26 | Replace the ABS blend with PP-T20 in the manufacture of the Front and Rear Door Panel Side Trims in MGI | nan | INR 147.0 | NG | nan | nan | nan
2311-IP-ID-12 | Replace PC-ABS used in the manufacture of Cup Holder Cover Mounts LH & RH within the IP assembly of MGI with standard ABS | Supplier evalutiaon | INR 76.0 | TBD | Supplier evalutiaon | Narendra | 2024-02-22 00:00:00
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-ET-ID-24 | 2311-IT-ID-22 | 2311-IP-ID-04 | 2311-SS-ID-04 | 2311-IP-ID-15 | 2311-IP-ID-02 | 2311-EL-ID-17 | 2311-DA-ID-34 | 2311-DA-ID-26 | 2311-IP-ID-12
Savings (INR) | 132 | 42 | 87 | 48 | 60 | 87 | 139 | 100 | 147 | 76
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 6 | 3
• Total Ideas: 10
• Total Potential Savings: INR 918.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 6
• Status NG: 3
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 918.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI