## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | Confirm on no part nuber change to avoid homologation cost | INR 115.0 | OK | Confirm on no part nuber change to avoid homologation cost | Nishant | 2024-06-17 00:00:00
2311-SS-ID-02 | 1. Reduce the width of the seat adjustment lever-2 from 345mm to 175mm commonising both. 2. Reduce the overall diameter of the bars from 13mm to 12mm. | Check for combined business case | INR 74.0 | NG | Check for combined business case | Kalp | 2023-11-07 00:00:00
2311-PRODUCT-ID-10 | Reduce the length of the Seat Release Straps found on the second and third-row seats | nan | INR 86.0 | NG | nan | nan | nan
2311-SS-ID-06 | Revise the existing seatbelt buckle housing brackets in MGI to match those in KIA, reducing the maximum width of the bracket from 33.5mm to 24mm, in line with KIA's design | nan | INR 93.0 | NG | nan | nan | nan
2311-PRODUCT-ID-09 | De-content the Plastic Protective Trims fitted onto the LHS and RHS mounting points of the third-row seats and cover the same with the fabric used on the vehicle floor. | Confirm on PTR plan | INR 76.0 | OK | Confirm on PTR plan | Harsh | 2024-06-14 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-03 | Substitute the Seatbelt Buckles used in the front row of the seating system in the vehicle with those employed in the second and third row LH and RH sides of the vehicle | nan | INR 126.0 | NG | nan | nan | nan
2311-SS-ID-11 | Process Deletion, Remove the Black Painting done on the Driver and Co-Driver Seat Base Support Frames | nan | INR 90.0 | NG | nan | nan | nan
2311-IT-ID-05 | Replace the TPE Coaster/Insert positioned at the base of the front centre armrest storage compartment with a Fabric one | nan | INR 40.0 | NG | nan | nan | nan
2311-SS-ID-07 | Replace the Steel Support Plates used within the second and third-row seating assemblies of MGI with Corrugated PP Panels as in KIA | Confirm on functionality requirement (load bearing capacity of seats) | INR 62.0 | NG | Confirm on functionality requirement (load bearing capacity of seats) | Nishant/ Ratnadeep | 2024-02-20 00:00:00
2311-SS-ID-04 | Substitute the leather upholstery on the left-hand (LH) and right-hand (RH) sides of the third-row seat bases with the same fabric utilized on the LH and RH sides of the corresponding backrests | Check for combined business case | INR 48.0 | NG | Check for combined business case | Kalp | 2023-11-10 00:00:00
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-07 | 2311-SS-ID-02 | 2311-PRODUCT-ID-10 | 2311-SS-ID-06 | 2311-PRODUCT-ID-09 | 2311-SS-ID-03 | 2311-SS-ID-11 | 2311-IT-ID-05 | 2311-SS-ID-07 | 2311-SS-ID-04
Savings (INR) | 115 | 74 | 86 | 93 | 76 | 126 | 90 | 40 | 62 | 48
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 2 | 0 | 8
• Total Ideas: 10
• Total Potential Savings: INR 810.00
• Implemented Ideas: 0
• Status OK: 2
• Status TBD: 0
• Status NG: 8
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 810.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI