## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-03 | Replace the rubber bushes used on the wiper blade mounting bolts with the plastic protective cap. | nan | INR 126.0 | NG | nan | nan | nan
2311-ET-ID-11 | 1. Remove the Foam inserts from both the LH and RH sides of MGI and use plastic trims instead as employed in KIA 2. Thinsulate could be used if required | nan | INR 131.0 | NG | nan | nan | nan
2311-ST-ID-05 | Redesign the current Steering Column to Steering Rack Linkage Plastic Trim and the Rubber Bush associated with a smaller setup as employed in KIA | nan | INR 98.0 | NG | nan | nan | nan
2311-FS-ID-01 | Remove the Neoprene Foam Sheaths present on the fuel lines and the fuel inlet hose of MGI | Confirm Kia routing photos for analysis with ASI | INR 142.0 | NG | Confirm Kia routing photos for analysis with ASI | Ratnadeep | 2024-02-12 00:00:00
2311-ST-ID-06 | Reduce the overall length and width of the rubber boots in MGI to match the dimensions of the similar rubber boots used in KIA | nan | INR 97.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-15 | De-content the rubber seal provided on the roller arm of each door | nan | INR 122.0 | NG | nan | nan | nan
2311-ET-ID-28 | Redesign the current Door Panel Exterior LH & RH Main Trims to a similar setup as employed in KIA, 1. Employ separate LH and RH Side Claddings (PP-T30) as in KIA 2. Reduce the current width of the Front and Rear Door Panel Exterior LH & RH Main Trims by 80mm and de-content the rubber seals used on all four doors | nan | INR 105.0 | TBD | nan | nan | nan
2311-DA-ID-01 | Reduce the overall width of the black vinyl pasted on the B-pillar from 70mm to 25mm | nan | INR 84.0 | NG | nan | nan | nan
2311-SS-ID-05 | 1. Replace the leather upholstery on the flaps located at the bottom of MGI's front-row seats with fabric 2. Use the same fabric (polyester) used to upholster the unexposed seat sides within MGI | one-pager for PP approval | INR 113.0 | NG | one-pager for PP approval | Ratnadeep | 2023-11-20 00:00:00
2311-DA-ID-17 | Instead of using Thinsulate within the door assemblies, Felt could be utilized | Confirm on part availability | INR 78.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-03 | 2311-ET-ID-11 | 2311-ST-ID-05 | 2311-FS-ID-01 | 2311-ST-ID-06 | 2311-PRODUCT-ID-15 | 2311-ET-ID-28 | 2311-DA-ID-01 | 2311-SS-ID-05 | 2311-DA-ID-17
Savings (INR) | 126 | 131 | 98 | 142 | 97 | 122 | 105 | 84 | 113 | 78
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 2 | 8
• Total Ideas: 10
• Total Potential Savings: INR 1,096.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 2
• Status NG: 8
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 1,096.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI