## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-27 | Replace the Thinsulate Acoustic Insulation used on the Front & Rear Wheel Arch LH & RH Liners for NVH restriction within MGI with Noiselite PP-PET Insulation | nan | INR 145.0 | TBD | nan | nan | nan
2311-IT-ID-26 | Replace PP-T20 with PP in the manufacture of the grab handles within the vehicle | nan | INR 145.0 | TBD | nan | nan | nan
2311-FS-ID-02 | Replace the Steel access cover used within MGI with a Plastic (PP(assumed)) one as used in KIA | Confirm technical feasibilty | INR 144.0 | TBD | Confirm technical feasibilty | Sumanta | 2024-04-23 00:00:00
2311-IT-ID-17 | Replace the Thinsulate used in between the Interior Trims of MGI with Felt | Confirm on part availability | INR 140.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
2311-EL-ID-25 | Replace Brass with Steel in the manufacture of the Main Terminal Connector Bolt within the Engine-Bay Fusebox Assembly of MGI | nan | INR 140.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IP-ID-16 | Replace PC-ABS with ABS in the manufacture of both Instrument Cluster Fascia Decorative Trim and the IP LHS & RHS Decorative Trims since the finish could be achieved on ABS-made trims as well | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 140.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-IP-ID-11 | Replace PC-ABS with PP-TD40 in the manufacture of the Front-Row Air Vent Casings in MGI | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 138.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-BIW-ID-06 | Reduce the Paint Coating Thickness of the highlighted Roof BiW Panel from 110 - 120μm to 70 - 80μm | nan | INR 135.0 | TBD | nan | nan | nan
2311-EL-ID-08 | Update the battery mounting technique in MGI to align with the one employed in KIA, including a redesign of the battery-securing enclosure. | nan | INR 135.0 | TBD | nan | nan | nan
2311-ET-ID-20 | Replace the PCB Module supplied by 'Taizhou Suzhong Antenna Group Co., Ltd.' used within the shark fin antenna of MGI with a similar one supplied by 'INFAC Elecs' used in KIA | nan | INR 133.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-24 | Redesign the current front logo assembly making the mentioned changes, 1. Remove the Logo Holder (Black) 2. Instead of chrome plating the Logo Holding Bracket, finish it in Black and snap-fit the logo M and G onto this 3. Introduce a new chrome-plated edge trim to complete the design | nan | INR 132.0 | TBD | nan | nan | nan
2311-IP-ID-01 | Replace the Thinsulate used within the LH & RH Centre Console Side Trims of MGI with Thermoplastic Felt | Confirm on part availability | INR 131.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
2311-WT-ID-01 | Replace the Tyre Pressure Monitoring System (TPMS) sensors from 'SGMW' used in MGI with similar sensors from 'Continental Engineering Services' used in KIA. | nan | INR 130.0 | TBD | nan | nan | nan
2311-BIW-ID-02 | Remove the black paint coating from the LH & RH A-Pillar Side Stiffener Brackets, LH & RH Centre Console and Gear Selector Base Mounting Brackets on the BIW of MGI | CFT buy off | INR 130.0 | TBD | CFT buy off | Ratnadeep | 2024-03-29 00:00:00
2311-EL-ID-23 | Replace the Mini (Closed) Fuses used within the Engine-Bay Fuse Box of the vehicle with Micro2 (Open) Fuses | nan | INR 127.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 5
Ideas Summary (Part 4)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-37 | Replace ABS with PP-T20 used in the manufacture of the LH and RH Mirror Outer Covers of MGI | nan | INR 127.0 | TBD | nan | nan | nan
2311-EL-ID-16 | Replace the Keyless Entry Sensor Module from Continental used in MGI with the one used in KIA | Confirm with homeroom on technical feasibility | INR 126.0 | TBD | Confirm with homeroom on technical feasibility | Ojaswini | TBC
2311-EL-ID-21 | Replace the Closed (Mini) Fuses used within the Engine-Bay Fuse Box of the vehicle with Open (Mini) Fuses | nan | INR 124.0 | TBD | nan | nan | nan
2311-ET-ID-26 | Replace POM with Glass Filled PP (PP-GF30) in the manufacture of the Rear Bumper Support Brackets 1 & 2 | nan | INR 124.0 | TBD | nan | nan | nan
2311-HV-ID-04 | Replace PC-ABS with PP-TD40 in the manufacture of the Second and Third-Row Air Vent Casings in MGI | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 123.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
Generated by VAVE-AI

## Slide 6
Ideas Summary (Part 5)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-BIW-ID-03 | Reduce the Paint Coating Thicknesses of the highlighted Front Fender and Rear Quarter Panel BiW Panels from 120 - 130μm to 85 - 95μm | nan | INR 122.0 | TBD | nan | nan | nan
2311-ET-ID-25 | Replace ABS with PP-T20 in the manufacture of the reflector casing | nan | INR 122.0 | TBD | nan | nan | nan
2311-EL-ID-20 | De-content the Door Lock Request Assembly along with the sensor within the co-driver door handle of the vehicle | nan | INR 122.0 | TBD | nan | nan | nan
2311-PA-ID-03 | Replace the current Accelerator Pedal Position Sensor used in MGI with a similar one used in KIA | nan | INR 122.0 | TBD | nan | nan | nan
2311-TA-ID-01 | Replace the PCB assembly from 'Continental' in MGI with a similar assembly as the one from 'Seoyon Electronics' used in KIA | nan | INR 121.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 7
Ideas Summary (Part 6)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PA-ID-01 | Remove the black paint coating on the Brake Pedal Mounting Bracket within MGI | nan | INR 115.0 | TBD | nan | nan | nan
2311-PA-ID-02 | Redesign the current Brake Pedal Mounting Bracket used in MGI to a similar bracket used in KIA. | nan | INR 113.0 | TBD | nan | nan | nan
2311-EL-ID-22 | Replace the Closed (Mini) Fuses used within the Driver-Side Fuse Box of the vehicle with Open (Mini) Fuses | nan | INR 111.0 | TBD | nan | nan | nan
2311-DA-ID-33 | Replace ABS with Talc Filled (20%) PP in the manufacture of the LH and RH Tailgate Outer Trim 2 Inner Trims | nan | INR 110.0 | TBD | nan | nan | nan
2311-ET-ID-28 | Redesign the current Door Panel Exterior LH & RH Main Trims to a similar setup as employed in KIA, 1. Employ separate LH and RH Side Claddings (PP-T30) as in KIA 2. Reduce the current width of the Front and Rear Door Panel Exterior LH & RH Main Trims by 80mm and de-content the rubber seals used on all four doors | nan | INR 105.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 8
Ideas Summary (Part 7)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-ET-ID-12 | Replace PC-ABS with ABS in the manufacture of the LH and RH Roof Rail End Covers 1 and 2 | HR feedback awaited | INR 102.0 | TBD | HR feedback awaited | Vikrant | 2024-02-22 00:00:00
2311-DA-ID-34 | Replace the Door Lock Request Sensor Assemblies used in MGI with the one used in KIA | nan | INR 100.0 | TBD | nan | nan | nan
2311-DA-ID-36 | Replace PP-T20 with PP in the manufacture of the LH and RH APS Trims | nan | INR 98.0 | TBD | nan | nan | nan
2311-ST-ID-02 | Replace PC-ABS with ABS in the manufacture of the Steering Wheel Top Trim 2 since the finish could be achieved on ABS-made trims as well | nan | INR 98.0 | TBD | nan | nan | nan
2311-DA-ID-32 | Replace ABS with Talc Filled (20%) PP in the manufacture of the LH and RH Side Spoiler Inner Trims | nan | INR 97.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 9
Ideas Summary (Part 8)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-BIW-ID-01 | 1. Reduce the width of the Frit Band application on the front windshield bottom of MGI from 165mm to 130mm as applied in KIA 2. Reduce the width of the Frit Band application on the rear windshield LH and RH sides of MGI from 195mm to 165mm as applied in KIA | nan | INR 96.0 | TBD | nan | nan | nan
2311-IP-ID-18 | Redesign the setup removing the entire reinforcement trim and combine the highlighted area shown in the picture into the Dashboard Assembly Upper Trim making it a single trim | nan | INR 96.0 | TBD | nan | nan | nan
2311-IT-ID-28 | Replace PP-TD10-GF10 with PP-T20 in the manufacture of the speaker casing. | nan | INR 94.0 | TBD | nan | nan | nan
2311-SS-ID-13 | Process Deletion, Remove the Black Painting done on the Third-Row Seat Mounting Frame | nan | INR 92.0 | TBD | nan | nan | nan
2311-PRODUCT-ID-12 | Decrease the width of the carpet by 100mm from the lower edge on the rear side of the trunk liner flap. | Confirm supplier feasibility in LC part for 5 seater | INR 90.0 | TBD | Confirm supplier feasibility in LC part for 5 seater | Akhil | 2024-06-28 00:00:00
Generated by VAVE-AI

## Slide 10
Ideas Summary (Part 9)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-11 | Reduce the width of the trunk liner flap by 60mm from the upper edge. | Confirm business case for 20mm reduction | INR 89.0 | TBD | Confirm business case for 20mm reduction | Kalp | 2024-02-14 00:00:00
2311-IP-ID-02 | Replace PC+ABS/TPU used in the manufacture of the Centre Console Bottle Holder Trim with PP | Supplier evalutiaon | INR 87.0 | TBD | Supplier evalutiaon | Narendra | 2024-02-22 00:00:00
2311-IP-ID-13 | Replace POM with PA6-GF30 in the manufacture of Glove Box Lock Pins 1 & 2 within the IP assembly of MGI | nan | INR 87.0 | TBD | nan | nan | nan
2311-IP-ID-19 | Replace the Thinsulate Acoustic Insulation used within the Dashboard and Control Panel for NVH restriction within MGI with Noiselite PP-PET Insulation as used in KIA | nan | INR 85.0 | TBD | nan | nan | nan
2311-BIW-ID-04 | Reduce the Paint Coating Thicknesses of the highlighted Front and Rear Door BiW Panels from 115 - 125μm to 80 - 90μm | nan | INR 84.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 11
Ideas Summary (Part 10)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-31 | Replace Glass Filled (15%) PP with Talc Filled (20%) PP in the manufacture of the Main Spoiler Inner Trim of MGI | nan | INR 83.0 | TBD | nan | nan | nan
2311-BIW-ID-05 | Reduce the Paint Coating Thickness of the highlighted Front Hood BiW Panel from 160 - 170μm to 100 - 110μm | nan | INR 82.0 | TBD | nan | nan | nan
2311-SS-ID-14 | Process Deletion, Remove the Black Painting done on the Second-Row Seat 60% and 40% Main Bracket Cross Members | nan | INR 81.0 | TBD | nan | nan | nan
2311-DA-ID-17 | Instead of using Thinsulate within the door assemblies, Felt could be utilized | Confirm on part availability | INR 78.0 | TBD | Confirm on part availability | Akhil/ Narendra | 29-Mar-24 16-Feb-24
2311-ST-ID-01 | Replace TPO with PP-T20 in the manufacture of the Steering Wheel Bottom Trim and the Steering Wheel Airbag Trim | nan | INR 77.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 12
Ideas Summary (Part 11)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Apply material optimization approach to analyze for cost reduction in MGI | Review feasibility with cross-functional team | ₹ 32 | AI-PROPOSAL | Review feasibility with cross-functional team | Digital Analyst | N/A
AI-GEN-01 | Apply material optimization approach to forward for cost reduction in MGI | Review feasibility with cross-functional team | ₹ 38 | AI-PROPOSAL | Review feasibility with cross-functional team | Digital Analyst | N/A
AI-GEN-01 | Apply material optimization approach to column for cost reduction in MGI | Review feasibility with cross-functional team | ₹ 44 | AI-PROPOSAL | Review feasibility with cross-functional team | Digital Analyst | N/A
AI-GEN-01 | Apply material optimization approach to ideas for cost reduction in MGI | Review feasibility with cross-functional team | ₹ 50 | AI-PROPOSAL | Review feasibility with cross-functional team | Digital Analyst | N/A
AI-GEN-01 | Apply material optimization approach to summarize for cost reduction in MGI | Review feasibility with cross-functional team | ₹ 56 | AI-PROPOSAL | Review feasibility with cross-functional team | Digital Analyst | N/A
Generated by VAVE-AI

## Slide 13: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-ET-ID-27 | 2311-IT-ID-26 | 2311-FS-ID-02 | 2311-IT-ID-17 | 2311-EL-ID-25 | 2311-IP-ID-16 | 2311-IP-ID-11 | 2311-BIW-ID-06 | 2311-EL-ID-08 | 2311-ET-ID-20 | 2311-ET-ID-24 | 2311-IP-ID-01 | 2311-WT-ID-01 | 2311-BIW-ID-02 | 2311-EL-ID-23 | 2311-DA-ID-37 | 2311-EL-ID-16 | 2311-EL-ID-21 | 2311-ET-ID-26 | 2311-HV-ID-04 | 2311-BIW-ID-03 | 2311-ET-ID-25 | 2311-EL-ID-20 | 2311-PA-ID-03 | 2311-TA-ID-01 | 2311-PA-ID-01 | 2311-PA-ID-02 | 2311-EL-ID-22 | 2311-DA-ID-33 | 2311-ET-ID-28 | 2311-ET-ID-12 | 2311-DA-ID-34 | 2311-DA-ID-36 | 2311-ST-ID-02 | 2311-DA-ID-32 | 2311-BIW-ID-01 | 2311-IP-ID-18 | 2311-IT-ID-28 | 2311-SS-ID-13 | 2311-PRODUCT-ID-12 | 2311-PRODUCT-ID-11 | 2311-IP-ID-02 | 2311-IP-ID-13 | 2311-IP-ID-19 | 2311-BIW-ID-04 | 2311-DA-ID-31 | 2311-BIW-ID-05 | 2311-SS-ID-14 | 2311-DA-ID-17 | 2311-ST-ID-01 | AI-GEN-01 | AI-GEN-01 | AI-GEN-01 | AI-GEN-01 | AI-GEN-01
Savings (INR) | 145 | 145 | 144 | 140 | 140 | 140 | 138 | 135 | 135 | 133 | 132 | 131 | 130 | 130 | 127 | 127 | 126 | 124 | 124 | 123 | 122 | 122 | 122 | 122 | 121 | 115 | 113 | 111 | 110 | 105 | 102 | 100 | 98 | 98 | 97 | 96 | 96 | 94 | 92 | 90 | 89 | 87 | 87 | 85 | 84 | 83 | 82 | 81 | 78 | 77 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 14: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 50 | 0
• Total Ideas: 55
• Total Potential Savings: INR 5,628.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 50
• Status NG: 0
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 15: Summary section
Total Ideas: 55 ideas analyzed.
Total Savings: INR 5,628.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI