## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-BIW-ID-05 | Reduce the Paint Coating Thickness of the highlighted Front Hood BiW Panel from 160 - 170μm to 100 - 110μm | nan | INR 82.0 | TBD | nan | nan | nan
2311-DA-ID-05 | Reduce the overall length of the plastic trim from 80mm to 30mm | nan | INR 104.0 | NG | nan | nan | nan
2311-DA-ID-06 | Replace the plastic trim used on the Hood Prop Rod in MGI with a foam cover trim as in KIA | Check supplier feasibility | INR 148.0 | NG | Check supplier feasibility | Chirag | 2024-02-16 00:00:00
2311-IT-ID-11 | Replace the 11-layer headliner used in MGI with a 10-layer headliner as in KIA | nan | INR 86.0 | NG | nan | nan | nan
2311-ET-ID-18 | Reduce the wall thickness of the Front and Rear Door Panel Exterior Main LH and RH Trims from 3mm to 2.8mm | New tooling cost from YFI to be confirmed for business case calculations | INR 67.0 | NG | New tooling cost from YFI to be confirmed for business case calculations | Akhil | 2024-02-12 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-02 | Replace the Plastic Caps mounted onto the doors, hood, and tailgate (total 14) with adhesive stickers. | nan | INR 130.0 | NG | nan | nan | nan
2311-EX-ID-06 | Reduce the average wall thickness of the Exhaust Pipes (Pre-Silencer Outlet Pipe, Flexi Exhaust Outlet Connecting Pipe and Main Silencer Inlet Pipe) in MGI from 1.8mm and 1.4mm to 1.2mm as seen in KIA | nan | INR 60.0 | NG | nan | nan | nan
2311-BIW-ID-07 | Reduce the Paint Coating Thickness of the highlighted Roof Side BiW Panels from 120 - 130μm to 100 - 110μm | nan | INR 71.0 | TBD | nan | nan | nan
2311-ET-ID-19 | Reduce the 2.4mm average wall thickness of the Windshield Cowl Trim in MGI to 2mm as in KIA | nan | INR 101.0 | NG | nan | nan | nan
2311-IP-ID-19 | Replace the Thinsulate Acoustic Insulation used within the Dashboard and Control Panel for NVH restriction within MGI with Noiselite PP-PET Insulation as used in KIA | nan | INR 85.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-BIW-ID-05 | 2311-DA-ID-05 | 2311-DA-ID-06 | 2311-IT-ID-11 | 2311-ET-ID-18 | 2311-PRODUCT-ID-02 | 2311-EX-ID-06 | 2311-BIW-ID-07 | 2311-ET-ID-19 | 2311-IP-ID-19
Savings (INR) | 82 | 104 | 148 | 86 | 67 | 130 | 60 | 71 | 101 | 85
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 3 | 7
• Total Ideas: 10
• Total Potential Savings: INR 934.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 3
• Status NG: 7
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 934.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI