## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EL-ID-10 | Replace the 444GSM Battery Insulation Cover used in MGI with a 350GSM Insulation Cover | Thermal performance pending with change in density | INR 61.0 | TBD | Thermal performance pending with change in density | Ojaswini | 2024-03-29 00:00:00
2311-EL-ID-08 | Update the battery mounting technique in MGI to align with the one employed in KIA, including a redesign of the battery-securing enclosure. | nan | INR 135.0 | TBD | nan | nan | nan
2311-EL-ID-09 | Remove the separate tray provided at the base of the battery enclosure in MGI | Confirm homeroom feasibility | INR 90.0 | NG | Confirm homeroom feasibility | Ratnadeep | 2024-04-15 00:00:00
2311-ET-ID-14 | 1. Replace the 2240GSM Engine Bay Insulation Cover within MGI with a 1080 - 1100GSM Insulation Cover (PES-NF) as in KIA 2. Replace the 5300GSM Cabin Insulation Cover within MGI with a 4550 - 4650GSM Insulation Cover as in KIA | Confirm on vehicel trial | INR 41.0 | OK | Confirm on vehicel trial | Narendra/ Ratnadeep | 2024-06-28 00:00:00
2311-EL-ID-11 | Replace PC-ABS with ABS in the manufacture of Tail Lamp Housings of MGI | nan | INR 137.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Transition the 'tell' component from a cast aluminum housing to a stamped steel or advanced polymer composite housing for weight and cost optimization. | Investigate the structural integrity and thermal dissipation capabilities of stamped steel and polymer composites under operational loads and thermal cycling. Finite Element Analysis (FEA) will be employed to simulate stress distribution and thermal gradients. Physical prototypes will undergo vibration, thermal shock, and mechanical load testing to validate performance against current aluminum specifications. Material characterization and cost analysis will confirm long-term viability. | 750000 | AI Proposal | Investigate the structural integrity and thermal dissipation capabilities of stamped steel and polymer composites under operational loads and thermal cycling. Finite Element Analysis (FEA) will be employed to simulate stress distribution and thermal gradients. Physical prototypes will undergo vibration, thermal shock, and mechanical load testing to validate performance against current aluminum specifications. Material characterization and cost analysis will confirm long-term viability. | VAVE | TBD
AI-GEN-02 | Implement a modular design for the 'tell' component, allowing for standardized sub-assemblies that can be sourced from multiple, competitive suppliers, rather than a single integrated unit. | Deconstruct the 'tell' component into its fundamental functional modules (e.g., actuator, sensor, control unit). Redesign interfaces and communication protocols to ensure interoperability between modules from different vendors. A thorough supplier qualification process will be established, including performance benchmarking and reliability testing of individual modules. Pilot production runs with mixed-sourced modules will be conducted to assess integration and overall system performance. | 900000 | AI Proposal | Deconstruct the 'tell' component into its fundamental functional modules (e.g., actuator, sensor, control unit). Redesign interfaces and communication protocols to ensure interoperability between modules from different vendors. A thorough supplier qualification process will be established, including performance benchmarking and reliability testing of individual modules. Pilot production runs with mixed-sourced modules will be conducted to assess integration and overall system performance. | VAVE | TBD
AI-GEN-03 | Replace the current multi-piece wiring harness for the 'tell' component with a consolidated, over-molded single harness assembly. | Analyze the existing wiring schematic and connector requirements. Design a consolidated harness with integrated connectors and strain relief. Utilize over-molding techniques to create a robust, single-piece unit. Validation will involve electrical continuity testing, impedance matching, environmental ingress protection (IP rating) testing, and vibration resistance testing to ensure signal integrity and durability comparable to or exceeding the current multi-piece solution. | 400000 | AI Proposal | Analyze the existing wiring schematic and connector requirements. Design a consolidated harness with integrated connectors and strain relief. Utilize over-molding techniques to create a robust, single-piece unit. Validation will involve electrical continuity testing, impedance matching, environmental ingress protection (IP rating) testing, and vibration resistance testing to ensure signal integrity and durability comparable to or exceeding the current multi-piece solution. | VAVE | TBD
AI-GEN-04 | Explore the use of additive manufacturing (3D printing) for complex internal features or customized brackets within the 'tell' component, enabling on-demand production and reduced tooling costs. | Identify design elements within the 'tell' component that benefit from complex geometries or low-volume customization. Select appropriate additive manufacturing materials (e.g., high-strength polymers, advanced alloys) and printing technologies. Validate printed parts through mechanical testing (tensile, flexural, impact) and functional fitment assessments. Conduct pilot studies to evaluate cost-effectiveness and lead times compared to traditional manufacturing methods for specific features. | 300000 | AI Proposal | Identify design elements within the 'tell' component that benefit from complex geometries or low-volume customization. Select appropriate additive manufacturing materials (e.g., high-strength polymers, advanced alloys) and printing technologies. Validate printed parts through mechanical testing (tensile, flexural, impact) and functional fitment assessments. Conduct pilot studies to evaluate cost-effectiveness and lead times compared to traditional manufacturing methods for specific features. | VAVE | TBD
AI-GEN-05 | Optimize the thermal management strategy of the 'tell' component by integrating passive cooling fins directly into the housing structure, eliminating separate heat sinks. | Conduct thermal simulations to determine optimal fin geometry and placement based on heat generation profiles of the 'tell' component's internal electronics. Analyze the manufacturability of integrated fins using chosen housing materials (e.g., die-casting, injection molding). Prototype parts will undergo thermal performance testing under various operating conditions, comparing surface temperatures and overall component reliability against current designs. Computational Fluid Dynamics (CFD) will be used to model airflow. | 500000 | AI Proposal | Conduct thermal simulations to determine optimal fin geometry and placement based on heat generation profiles of the 'tell' component's internal electronics. Analyze the manufacturability of integrated fins using chosen housing materials (e.g., die-casting, injection molding). Prototype parts will undergo thermal performance testing under various operating conditions, comparing surface temperatures and overall component reliability against current designs. Computational Fluid Dynamics (CFD) will be used to model airflow. | VAVE | TBD
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-06 | Reduce the number of fasteners and assembly steps required for the 'tell' component by designing snap-fit or interlocking features into its sub-assemblies. | Analyze the current assembly process and identify opportunities for integrating mechanical locking mechanisms. Design and prototype snap-fit features, ensuring sufficient retention force and resistance to vibration and thermal cycling. Validation will involve repeated assembly/disassembly cycles, pull-off force testing, and environmental testing to confirm the integrity of the interlocking features throughout the component's lifecycle. Torque and force analysis will inform design parameters. | 600000 | AI Proposal | Analyze the current assembly process and identify opportunities for integrating mechanical locking mechanisms. Design and prototype snap-fit features, ensuring sufficient retention force and resistance to vibration and thermal cycling. Validation will involve repeated assembly/disassembly cycles, pull-off force testing, and environmental testing to confirm the integrity of the interlocking features throughout the component's lifecycle. Torque and force analysis will inform design parameters. | VAVE | TBD
WEB-GEN-01 | Improve cross-functional team collaboration for design and technical teams. | Implement structured workshops and joint development sessions between design and technical engineering teams to foster better understanding and alignment. This can lead to more efficient design iterations, reduced rework, and optimized material selection early in the development cycle, potentially impacting the 'mg' component by ensuring its design integrates seamlessly with other systems, thus reducing complexity and manufacturing costs. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | 0 | Web Sourced | Implement structured workshops and joint development sessions between design and technical engineering teams to foster better understanding and alignment. This can lead to more efficient design iterations, reduced rework, and optimized material selection early in the development cycle, potentially impacting the 'mg' component by ensuring its design integrates seamlessly with other systems, thus reducing complexity and manufacturing costs. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | VAVE | TBD
WEB-GEN-02 | Leverage data analytics for performance optimization and component lifecycle management. | Establish a robust data acquisition and analysis framework to monitor the performance and wear characteristics of the 'mg' component in real-time. Analyzing this data can identify suboptimal operating conditions or predict potential failures, allowing for proactive maintenance or design modifications that extend component lifespan and reduce replacement costs. Source: https://www.f1technical.net/forum/viewtopic.php?t=32051&start=7125 | 0 | Web Sourced | Establish a robust data acquisition and analysis framework to monitor the performance and wear characteristics of the 'mg' component in real-time. Analyzing this data can identify suboptimal operating conditions or predict potential failures, allowing for proactive maintenance or design modifications that extend component lifespan and reduce replacement costs. Source: https://www.f1technical.net/forum/viewtopic.php?t=32051&start=7125 | VAVE | TBD
Generated by VAVE-AI

## Slide 5: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-EL-ID-10 | 2311-EL-ID-08 | 2311-EL-ID-09 | 2311-ET-ID-14 | 2311-EL-ID-11 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03 | AI-GEN-04 | AI-GEN-05 | AI-GEN-06 | WEB-GEN-01 | WEB-GEN-02
Savings (INR) | 61 | 135 | 90 | 41 | 137 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 6: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 1 | 2 | 2
• Total Ideas: 13
• Total Potential Savings: INR 464.00
• Implemented Ideas: 0
• Status OK: 1
• Status TBD: 2
• Status NG: 2
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 7: Summary section
Total Ideas: 13 ideas analyzed.
Total Savings: INR 464.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI