## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-02 | Replace the Plastic Caps mounted onto the doors, hood, and tailgate (total 14) with adhesive stickers. | nan | INR 130.0 | NG | nan | nan | nan
2311-BIW-ID-03 | Reduce the Paint Coating Thicknesses of the highlighted Front Fender and Rear Quarter Panel BiW Panels from 120 - 130μm to 85 - 95μm | nan | INR 122.0 | TBD | nan | nan | nan
2311-BIW-ID-05 | Reduce the Paint Coating Thickness of the highlighted Front Hood BiW Panel from 160 - 170μm to 100 - 110μm | nan | INR 82.0 | TBD | nan | nan | nan
2311-IT-ID-05 | Replace the TPE Coaster/Insert positioned at the base of the front centre armrest storage compartment with a Fabric one | nan | INR 40.0 | NG | nan | nan | nan
2311-IT-ID-22 | Replace PP-T20 used in the manufacture of the Third Row LH & RH Cup Holders with PP | nan | INR 42.0 | TBD | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-11 | Process Deletion, Remove the Black Painting done on the Driver and Co-Driver Seat Base Support Frames | nan | INR 90.0 | NG | nan | nan | nan
2311-ET-ID-11 | 1. Remove the Foam inserts from both the LH and RH sides of MGI and use plastic trims instead as employed in KIA 2. Thinsulate could be used if required | nan | INR 131.0 | NG | nan | nan | nan
2311-PRODUCT-ID-24 | Eliminate the hooks from the receptacle trims found on the RH side of the headrest assemblies reducing the overall length from 53.3mm to 40mm | nan | INR 64.0 | NG | nan | nan | nan
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | Confirm on no part nuber change to avoid homologation cost | INR 115.0 | OK | Confirm on no part nuber change to avoid homologation cost | Nishant | 2024-06-17 00:00:00
2311-SS-ID-06 | Revise the existing seatbelt buckle housing brackets in MGI to match those in KIA, reducing the maximum width of the bracket from 33.5mm to 24mm, in line with KIA's design | nan | INR 93.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-02 | 2311-BIW-ID-03 | 2311-BIW-ID-05 | 2311-IT-ID-05 | 2311-IT-ID-22 | 2311-SS-ID-11 | 2311-ET-ID-11 | 2311-PRODUCT-ID-24 | 2311-PRODUCT-ID-07 | 2311-SS-ID-06
Savings (INR) | 130 | 122 | 82 | 40 | 42 | 90 | 131 | 64 | 115 | 93
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 1 | 3 | 6
• Total Ideas: 10
• Total Potential Savings: INR 909.00
• Implemented Ideas: 0
• Status OK: 1
• Status TBD: 3
• Status NG: 6
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 909.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI