## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-WT-ID-03 | De-content the spare wheel provided with the vehicle | nan | INR 57.0 | TBD | nan | nan | nan
2311-PRODUCT-ID-11 | Reduce the width of the trunk liner flap by 60mm from the upper edge. | Confirm business case for 20mm reduction | INR 89.0 | TBD | Confirm business case for 20mm reduction | Kalp | 2024-02-14 00:00:00
2311-PRODUCT-ID-23 | Redesign the Tailgate Bumper Stops in MGI into an 'L' shape reducing the length from 74mm to 40mm | 1. Confirm with homeroom 2. Confirm for cost saving and tooling requirement.Homeroom ideas to be bunched up and taken up for implementation at program level | INR 71.0 | NG | 1. Confirm with homeroom 2. Confirm for cost saving and tooling requirement.Homeroom ideas to be bunched up and taken up for implementation at program level | 1.Himanshu 2. Sruhti | nan
2311-ST-ID-06 | Reduce the overall length and width of the rubber boots in MGI to match the dimensions of the similar rubber boots used in KIA | nan | INR 97.0 | NG | nan | nan | nan
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | Confirm on no part nuber change to avoid homologation cost | INR 115.0 | OK | Confirm on no part nuber change to avoid homologation cost | Nishant | 2024-06-17 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-16 | Replace fiberboard with velcro tape and carpet in the assembly | Check for loss in functionality | INR 64.0 | TBD | Check for loss in functionality | Narendra | 2024-02-22 00:00:00
2311-ET-ID-16 | Reduce the wall thickness of the Front Wheel Arch Liners present on both LH and RH sides from 1.6mm to 1.4mm | nan | INR 92.0 | NG | nan | nan | nan
2311-SP-ID-01 | 1. Reduce the overall wall thickness of the Brake Dust Cover Plates present on all four wheel hubs of the vehicles from 1mm to 0.8mm 2. Reduce the paint coating thickness on each side of all four plates from 56 microns to 27.8 microns | nan | INR 57.0 | NG | nan | nan | nan
2311-ST-ID-02 | Replace PC-ABS with ABS in the manufacture of the Steering Wheel Top Trim 2 since the finish could be achieved on ABS-made trims as well | nan | INR 98.0 | TBD | nan | nan | nan
2311-ST-ID-04 | Reduce the length of the Iron Castings from 175mm to 110mm and Increase the length of the Rods to compensate instead, similar to the setup employed in KIA | nan | INR 122.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-WT-ID-03 | 2311-PRODUCT-ID-11 | 2311-PRODUCT-ID-23 | 2311-ST-ID-06 | 2311-PRODUCT-ID-07 | 2311-PRODUCT-ID-16 | 2311-ET-ID-16 | 2311-SP-ID-01 | 2311-ST-ID-02 | 2311-ST-ID-04
Savings (INR) | 57 | 89 | 71 | 97 | 115 | 64 | 92 | 57 | 98 | 122
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 1 | 4 | 5
• Total Ideas: 10
• Total Potential Savings: INR 862.00
• Implemented Ideas: 0
• Status OK: 1
• Status TBD: 4
• Status NG: 5
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 862.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI