## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-01 | Replace the dual LED lamps used for rear license plate illumination with a pair of single LED lamps. | N/A | INR 68.00 | NG | N/A | N/A | N/A
2311-PRODUCT-ID-07 | De-content the plastic trims found protecting the top tethers from both sides of the seat as the tethers could be placed within the seat fabric itself and a slit on the same could facilitate easy access | N/A | INR 115.00 | OK | N/A | N/A | N/A
2311-PRODUCT-ID-09 | De-content the Plastic Protective Trims fitted onto the LHS and RHS mounting points of the third-row seats and cover the same with the fabric used on the vehicle floor. | N/A | INR 76.00 | OK | N/A | N/A | N/A
2311-PRODUCT-ID-14 | Reduce the thickness of the rear wiper pivot bolt cover trim from 2mm to 1.3mm. | N/A | INR 46.00 | TBD | N/A | N/A | N/A
2311-PRODUCT-ID-16 | Replace fiberboard with velcro tape and carpet in the assembly | N/A | INR 64.00 | TBD | N/A | N/A | N/A
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-17 | 1. Relocate the Battery Negative Terminal Earthing Wire mount from the side to the top of the front suspension subframe of the vehicle 2. Reduce the length of the connector terminal and instead of using two bolts, use a single bolt 3. Reduce the overall size and wall thickness of the Battery Negative Terminal Cast Clamp | N/A | INR 103.00 | Hold | N/A | N/A | N/A
2311-PRODUCT-ID-21 | De-content the Spacer Plates mounted onto the door frame and if required, increase the length of the latch receiver on the Striker Plate to ensure the doors close smoothly and securely | N/A | INR 65.00 | NG | N/A | N/A | N/A
2311-PRODUCT-ID-22 | De-content the plastic support trims found within the storage pocket flaps behind the LH and RH front seats | N/A | INR 108.00 | NG | N/A | N/A | N/A
2311-BA-ID-02 | Remove the black paint coating from the Brake Caliper Mounting Brackets on all four brake assemblies of MGI, following the procedure used for the front brake caliper mounting brackets in KIA. | N/A | INR 102.00 | NG | N/A | N/A | N/A
2311-DA-ID-07 | Replace PA6-GF30 with PA6-GF20 in the manufacture of the Tailgate Release/Handle Trim | N/A | INR 143.00 | NG | N/A | N/A | N/A
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-DA-ID-15 | Replace PC-ABS with ABS in the manufacture of Speaker Trims present on the door assemblies. | N/A | INR 51.00 | NG | N/A | N/A | N/A
2311-DA-ID-20 | De-content Cable Protective Sheaths one each from all the Lock Release and Front Window Regulator assemblies of the vehicle | N/A | INR 129.00 | NG | N/A | N/A | N/A
2311-EL-ID-01 | Replace the 16-pin connector set used on the IRVM assembly with an 8-pin connector set. | N/A | INR 142.00 | NG | N/A | N/A | N/A
2311-EL-ID-10 | Replace the 444GSM Battery Insulation Cover used in MGI with a 350GSM Insulation Cover | N/A | INR 61.00 | TBD | N/A | N/A | N/A
2311-EL-ID-15 | Replace the 'Roots Windtone 75' horns used in MGI with 'A78SE's used in KIA | N/A | INR 58.00 | TBD | N/A | N/A | N/A
Generated by VAVE-AI

## Slide 5
Ideas Summary (Part 4)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EL-ID-16 | Replace the Keyless Entry Sensor Module from Continental used in MGI with the one used in KIA | N/A | INR 126.00 | TBD | N/A | N/A | N/A
2311-EL-ID-17 | Replace the oxygen sensors used in MGI with the oxygen sensors used in KIA | N/A | INR 139.00 | Hold | N/A | N/A | N/A
2311-ET-ID-12 | Replace PC-ABS with ABS in the manufacture of the LH and RH Roof Rail End Covers 1 and 2 | N/A | INR 102.00 | TBD | N/A | N/A | N/A
2311-ET-ID-15 | De-content the Cowl Panel NVH Insulation from the engine bay of MGI | N/A | INR 126.00 | OK | N/A | N/A | N/A
2311-FS-ID-02 | Replace the Steel access cover used within MGI with a Plastic (PP(assumed)) one as used in KIA | N/A | INR 144.00 | TBD | N/A | N/A | N/A
Generated by VAVE-AI

## Slide 6
Ideas Summary (Part 5)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Extend fastener optimization approach #1 for PE | N/A | INR 88.56 | N/A | N/A | N/A | N/A
AI-GEN-02 | Extend fastener optimization approach #2 for PE | N/A | INR 93.48 | N/A | N/A | N/A | N/A
AI-GEN-03 | Extend fastener optimization approach #3 for PE | N/A | INR 98.40 | N/A | N/A | N/A | N/A
Generated by VAVE-AI

## Slide 7: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-01 | 2311-PRODUCT-ID-07 | 2311-PRODUCT-ID-09 | 2311-PRODUCT-ID-14 | 2311-PRODUCT-ID-16 | 2311-PRODUCT-ID-17 | 2311-PRODUCT-ID-21 | 2311-PRODUCT-ID-22 | 2311-BA-ID-02 | 2311-DA-ID-07 | 2311-DA-ID-15 | 2311-DA-ID-20 | 2311-EL-ID-01 | 2311-EL-ID-10 | 2311-EL-ID-15 | 2311-EL-ID-16 | 2311-EL-ID-17 | 2311-ET-ID-12 | 2311-ET-ID-15 | 2311-FS-ID-02 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03
Savings (INR) | 68 | 115 | 76 | 46 | 64 | 103 | 65 | 108 | 102 | 143 | 51 | 129 | 142 | 61 | 58 | 126 | 139 | 102 | 126 | 144 | 88.56 | 93.48 | 98.4
Generated by VAVE-AI

## Slide 8: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 3 | 7 | 8
• Total Ideas: 23
• Total Potential Savings: INR 2,248.44
• Implemented Ideas: 0
• Status OK: 3
• Status TBD: 7
• Status NG: 8
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 9: Summary section
Total Ideas: 23 ideas analyzed.
Total Savings: INR 2,248.44 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI