## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EL-ID-10 | Replace the 444GSM Battery Insulation Cover used in MGI with a 350GSM Insulation Cover | Thermal performance pending with change in density | INR 61.0 | TBD | Thermal performance pending with change in density | Ojaswini | 2024-03-29 00:00:00
2311-EL-ID-08 | Update the battery mounting technique in MGI to align with the one employed in KIA, including a redesign of the battery-securing enclosure. | nan | INR 135.0 | TBD | nan | nan | nan
2311-EL-ID-09 | Remove the separate tray provided at the base of the battery enclosure in MGI | Confirm homeroom feasibility | INR 90.0 | NG | Confirm homeroom feasibility | Ratnadeep | 2024-04-15 00:00:00
2311-ET-ID-14 | 1. Replace the 2240GSM Engine Bay Insulation Cover within MGI with a 1080 - 1100GSM Insulation Cover (PES-NF) as in KIA 2. Replace the 5300GSM Cabin Insulation Cover within MGI with a 4550 - 4650GSM Insulation Cover as in KIA | Confirm on vehicel trial | INR 41.0 | OK | Confirm on vehicel trial | Narendra/ Ratnadeep | 2024-06-28 00:00:00
2311-EL-ID-11 | Replace PC-ABS with ABS in the manufacture of Tail Lamp Housings of MGI | nan | INR 137.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Implement a direct-injection cooling system for the battery pack, eliminating the need for a separate coolant pump and reservoir by utilizing the vehicle's primary coolant loop and a heat exchanger integrated directly into the battery casing. | This approach leverages existing thermal management infrastructure. The physics involves convective heat transfer from the battery cells to the coolant flowing through integrated channels. Validation will require CFD analysis to model thermal gradients under various load conditions, followed by physical testing of a prototype pack under accelerated life cycle testing and extreme temperature scenarios to confirm thermal stability and prevent thermal runaway. | 1500000 | AI Proposal | This approach leverages existing thermal management infrastructure. The physics involves convective heat transfer from the battery cells to the coolant flowing through integrated channels. Validation will require CFD analysis to model thermal gradients under various load conditions, followed by physical testing of a prototype pack under accelerated life cycle testing and extreme temperature scenarios to confirm thermal stability and prevent thermal runaway. | VAVE | TBD
AI-GEN-02 | Substitute the current multi-piece battery enclosure with a single-piece, high-strength composite structure manufactured using advanced composite molding techniques (e.g., RTM or compression molding), thereby reducing assembly complexity and the number of fasteners. | The core principle here is to simplify the supply chain and manufacturing process. A single-piece design inherently reduces assembly labor and the potential for leaks or structural weaknesses at joints. Validation will involve Finite Element Analysis (FEA) to assess structural integrity under crash loads and vibration, alongside material testing to confirm long-term durability and environmental resistance of the chosen composite. | 1200000 | AI Proposal | The core principle here is to simplify the supply chain and manufacturing process. A single-piece design inherently reduces assembly labor and the potential for leaks or structural weaknesses at joints. Validation will involve Finite Element Analysis (FEA) to assess structural integrity under crash loads and vibration, alongside material testing to confirm long-term durability and environmental resistance of the chosen composite. | VAVE | TBD
AI-GEN-03 | Redesign the battery module interconnects from traditional bolted busbars to a laser-welded or ultrasonic-welded tab system, reducing material usage and improving electrical conductivity. | This proposal focuses on optimizing the electrical path and reducing material waste. Welding offers a more robust and lower-resistance connection compared to bolted joints, potentially improving energy efficiency. Validation will involve cyclic stress testing of the welded joints to assess fatigue life, electrochemical impedance spectroscopy (EIS) to measure resistance changes over time, and thermal imaging during high current discharge to monitor for hot spots. | 800000 | AI Proposal | This proposal focuses on optimizing the electrical path and reducing material waste. Welding offers a more robust and lower-resistance connection compared to bolted joints, potentially improving energy efficiency. Validation will involve cyclic stress testing of the welded joints to assess fatigue life, electrochemical impedance spectroscopy (EIS) to measure resistance changes over time, and thermal imaging during high current discharge to monitor for hot spots. | VAVE | TBD
AI-GEN-04 | Integrate the Battery Management System (BMS) control electronics directly onto the battery module busbars or cell holders, eliminating the need for separate printed circuit boards (PCBs) and associated wiring harnesses. | The objective is to miniaturize and consolidate electronic components. By integrating the BMS directly, we reduce the Bill of Materials (BOM) for PCBs and connectors, and simplify assembly. Validation will involve rigorous EMI/EMC testing to ensure the integrated electronics are not susceptible to interference, and thermal simulation to confirm that the heat generated by the electronics is adequately dissipated by the battery module itself. | 1000000 | AI Proposal | The objective is to miniaturize and consolidate electronic components. By integrating the BMS directly, we reduce the Bill of Materials (BOM) for PCBs and connectors, and simplify assembly. Validation will involve rigorous EMI/EMC testing to ensure the integrated electronics are not susceptible to interference, and thermal simulation to confirm that the heat generated by the electronics is adequately dissipated by the battery module itself. | VAVE | TBD
AI-GEN-05 | Explore the use of a lower-density, but still functionally equivalent, thermal interface material (TIM) between battery cells and the cooling plates, based on advanced polymer composites with tailored thermal conductivity. | This idea targets cost reduction through material optimization. The physics of heat transfer dictates that the TIM's thermal resistance is critical. By identifying a TIM with lower density but sufficient thermal conductivity, we can reduce material cost and weight. Validation will involve comparative thermal performance testing of different TIMs under controlled conditions, measuring cell temperatures during charge/discharge cycles, and assessing long-term aging of the TIM. | 600000 | AI Proposal | This idea targets cost reduction through material optimization. The physics of heat transfer dictates that the TIM's thermal resistance is critical. By identifying a TIM with lower density but sufficient thermal conductivity, we can reduce material cost and weight. Validation will involve comparative thermal performance testing of different TIMs under controlled conditions, measuring cell temperatures during charge/discharge cycles, and assessing long-term aging of the TIM. | VAVE | TBD
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-06 | Implement a modular cell-to-pack (CTP) design where individual battery cells are directly integrated into the battery pack structure, bypassing intermediate module housings and simplifying the overall assembly. | The fundamental principle is to reduce component count and assembly steps. CTP designs eliminate module casings, interconnects between modules, and associated assembly labor, leading to significant cost and weight savings. Validation will focus on ensuring structural integrity of the pack without modules, thermal management effectiveness of direct cell cooling, and robustness against vibration and shock through extensive mechanical and environmental testing. | 2000000 | AI Proposal | The fundamental principle is to reduce component count and assembly steps. CTP designs eliminate module casings, interconnects between modules, and associated assembly labor, leading to significant cost and weight savings. Validation will focus on ensuring structural integrity of the pack without modules, thermal management effectiveness of direct cell cooling, and robustness against vibration and shock through extensive mechanical and environmental testing. | VAVE | TBD
WEB-GEN-01 | Improve cross-functional team collaboration for design efficiency | Implement structured workshops and integrated software platforms to foster better communication and understanding between design and technical teams. This can identify design simplifications or material substitutions early in the development cycle, reducing rework and material waste. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | 0 | Web Sourced | Implement structured workshops and integrated software platforms to foster better communication and understanding between design and technical teams. This can identify design simplifications or material substitutions early in the development cycle, reducing rework and material waste. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | VAVE | TBD
WEB-GEN-02 | Streamline livery application processes | Analyze current livery application methods and explore alternative materials or application techniques that reduce labor, material waste, or processing time. This could involve investigating advanced vinyl wrapping technologies or more efficient paint systems if applicable to the 'mg' component. Source: https://www.f1technical.net/forum/viewtopic.php?t=32054&start=7500 | 0 | Web Sourced | Analyze current livery application methods and explore alternative materials or application techniques that reduce labor, material waste, or processing time. This could involve investigating advanced vinyl wrapping technologies or more efficient paint systems if applicable to the 'mg' component. Source: https://www.f1technical.net/forum/viewtopic.php?t=32054&start=7500 | VAVE | TBD
Generated by VAVE-AI

## Slide 5: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-EL-ID-10 | 2311-EL-ID-08 | 2311-EL-ID-09 | 2311-ET-ID-14 | 2311-EL-ID-11 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03 | AI-GEN-04 | AI-GEN-05 | AI-GEN-06 | WEB-GEN-01 | WEB-GEN-02
Savings (INR) | 61 | 135 | 90 | 41 | 137 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 6: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 1 | 2 | 2
• Total Ideas: 13
• Total Potential Savings: INR 464.00
• Implemented Ideas: 0
• Status OK: 1
• Status TBD: 2
• Status NG: 2
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 7: Summary section
Total Ideas: 13 ideas analyzed.
Total Savings: INR 464.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI