## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-21 | De-content the Spacer Plates mounted onto the door frame and if required, increase the length of the latch receiver on the Striker Plate to ensure the doors close smoothly and securely | Share design change for business case evaluation | INR 65.0 | NG | Share design change for business case evaluation | Manish Jaju | 2023-12-12 00:00:00
2311-PRODUCT-ID-14 | Reduce the thickness of the rear wiper pivot bolt cover trim from 2mm to 1.3mm. | Confirm with homeroom on technical feasibility & Confirm localization | INR 46.0 | TBD | Confirm with homeroom on technical feasibility & Confirm localization | Ojaswini | 2023-12-14 00:00:00
2311-IP-ID-13 | Replace POM with PA6-GF30 in the manufacture of Glove Box Lock Pins 1 & 2 within the IP assembly of MGI | nan | INR 87.0 | TBD | nan | nan | nan
2311-PRODUCT-ID-06 | Change the design of the lug nut used in MGI with the design of the lug nut used in KIA. Wheel lug nut in MGI- Overall length - 31.3mm Thread length - 27.95mm Wheel lug nut in KIA- Overall length - 27.5mm Thread length - 15mm | nan | INR 50.0 | NG | nan | nan | nan
2311-PRODUCT-ID-17 | 1. Relocate the Battery Negative Terminal Earthing Wire mount from the side to the top of the front suspension subframe of the vehicle 2. Reduce the length of the connector terminal and instead of using two bolts, use a single bolt 3. Reduce the overall size and wall thickness of the Battery Negative Terminal Cast Clamp | Homeroom ideas to be bunched up and taken up for implementation at program level. Confirm localization feasibility | INR 103.0 | Hold | Homeroom ideas to be bunched up and taken up for implementation at program level. Confirm localization feasibility | Ojaswini | 2023-12-20 00:00:00
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-SS-ID-06 | Revise the existing seatbelt buckle housing brackets in MGI to match those in KIA, reducing the maximum width of the bracket from 33.5mm to 24mm, in line with KIA's design | nan | INR 93.0 | NG | nan | nan | nan
2311-EL-ID-08 | Update the battery mounting technique in MGI to align with the one employed in KIA, including a redesign of the battery-securing enclosure. | nan | INR 135.0 | TBD | nan | nan | nan
2311-PRODUCT-ID-03 | Replace the rubber bushes used on the wiper blade mounting bolts with the plastic protective cap. | nan | INR 126.0 | NG | nan | nan | nan
2311-EX-ID-02 | Replace the steel rods used in the fabrication of the exhaust hanger mounting brackets in MGI with hollow steel pipes as used in KIA | nan | INR 62.0 | NG | nan | nan | nan
2311-PRODUCT-ID-02 | Replace the Plastic Caps mounted onto the doors, hood, and tailgate (total 14) with adhesive stickers. | nan | INR 130.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-21 | 2311-PRODUCT-ID-14 | 2311-IP-ID-13 | 2311-PRODUCT-ID-06 | 2311-PRODUCT-ID-17 | 2311-SS-ID-06 | 2311-EL-ID-08 | 2311-PRODUCT-ID-03 | 2311-EX-ID-02 | 2311-PRODUCT-ID-02
Savings (INR) | 65 | 46 | 87 | 50 | 103 | 93 | 135 | 126 | 62 | 130
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 3 | 6
• Total Ideas: 10
• Total Potential Savings: INR 897.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 3
• Status NG: 6
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 897.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI