## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-PRODUCT-ID-02 | Replace the Plastic Caps mounted onto the doors, hood, and tailgate (total 14) with adhesive stickers. | nan | INR 130.0 | NG | nan | nan | nan
2311-PRODUCT-ID-23 | Redesign the Tailgate Bumper Stops in MGI into an 'L' shape reducing the length from 74mm to 40mm | 1. Confirm with homeroom 2. Confirm for cost saving and tooling requirement.Homeroom ideas to be bunched up and taken up for implementation at program level | INR 71.0 | NG | 1. Confirm with homeroom 2. Confirm for cost saving and tooling requirement.Homeroom ideas to be bunched up and taken up for implementation at program level | 1.Himanshu 2. Sruhti | nan
VAVE-SWI-056 | Quarter Lower Insulation removal | Complete NVH trial | INR 0.0 | OK | Complete NVH trial | Narendra/ Ratnadeep | 2024-06-21 00:00:00
2311-ET-ID-25 | Replace ABS with PP-T20 in the manufacture of the reflector casing | nan | INR 122.0 | TBD | nan | nan | nan
2311-FS-ID-03 | Reduce the average wall thickness of the Baffle Plates present within the fuel tank assembly of MGI from 0.7mm to 0.6mm as seen in the fuel tank assembly of KIA | nan | INR 75.0 | NG | nan | nan | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-IP-ID-11 | Replace PC-ABS with PP-TD40 in the manufacture of the Front-Row Air Vent Casings in MGI | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | INR 138.0 | TBD | Potential saving evaluation of RM level is required to take this with SGMW for further discussions. | Kalp | nan
2311-EL-ID-07 | Replace PP-T30 used in the manufacture of the LH and RH DRL/Indicator Lamp Housings of MGI with PP-TD20 | nan | INR 79.0 | NG | nan | nan | nan
VAVE-SWI-052 | Console Armrest rear panel wrapping to MIC | Confirm with supplier on 55lakh investment requirement | INR 0.0 | NG | Confirm with supplier on 55lakh investment requirement | Akhil | 2024-06-07 00:00:00
VAVE-SWI-047 | Hydrography to painting | Confirm on plate availability for appearnace approval | INR 0.0 | OK | Confirm on plate availability for appearnace approval | Narendra | 2024-06-15 00:00:00
2311-IP-ID-07 | Replace PP+EPDM+T20 with PP+T20 in the manufacture of the dashboard middle trim of the vehicle | To be considered for new project | INR 59.0 | NG | To be considered for new project | Ratnadeep | nan
Generated by VAVE-AI

## Slide 4: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-PRODUCT-ID-02 | 2311-PRODUCT-ID-23 | VAVE-SWI-056 | 2311-ET-ID-25 | 2311-FS-ID-03 | 2311-IP-ID-11 | 2311-EL-ID-07 | VAVE-SWI-052 | VAVE-SWI-047 | 2311-IP-ID-07
Savings (INR) | 130 | 71 | 0 | 122 | 75 | 138 | 79 | 0 | 0 | 59
Generated by VAVE-AI

## Slide 5: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 2 | 2 | 6
• Total Ideas: 10
• Total Potential Savings: INR 674.00
• Implemented Ideas: 0
• Status OK: 2
• Status TBD: 2
• Status NG: 6
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 6: Summary section
Total Ideas: 10 ideas analyzed.
Total Savings: INR 674.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI