## Slide 1
JSW MG MOTOR INDIA
Cost Reduction Idea Analysis Presentation
Presentation generated by VAVE AI
Generated by VAVE-AI

## Slide 2
Ideas Summary (Part 1)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
2311-EL-ID-18 | Replace the Auto Headlamp Photodiode Sensor used in MGI with the one used in KIA. | nan | INR 42.0 | TBD | nan | nan | nan
2311-EL-ID-06 | Replace PP-T30 used in the manufacture of the LH and RH Headlamp Housings of MGI with PP-TD20 as used in KIA | nan | INR 126.0 | NG | nan | nan | nan
2311-IT-ID-19 | Process Deletion, Remove the Anodizing done on the LH & RH Sunroof Guide Rails in MGI | Homeroom ideas to be bunched up and taken up for implementation at program level | INR 56.0 | Hold | Homeroom ideas to be bunched up and taken up for implementation at program level | Manish Jaju | 2024-02-20 00:00:00
2311-PRODUCT-ID-24 | Eliminate the hooks from the receptacle trims found on the RH side of the headrest assemblies reducing the overall length from 53.3mm to 40mm | nan | INR 64.0 | NG | nan | nan | nan
2311-PRODUCT-ID-01 | Replace the dual LED lamps used for rear license plate illumination with a pair of single LED lamps. | Homeroom ideas to be bunched up and taken up for implementation at program level | INR 68.0 | NG | Homeroom ideas to be bunched up and taken up for implementation at program level | Ojaswini | nan
Generated by VAVE-AI

## Slide 3
Ideas Summary (Part 2)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-01 | Replace the integrated LED tail lamp module with a modular design comprising separate LED arrays for brake, turn, and reverse functions, utilizing standard, off-the-shelf LED components and a simpler, more cost-effective PCB. | The current integrated LED tail lamp module likely involves complex custom PCB design and specialized LED integration, driving up tooling and per-unit costs. By adopting a modular approach, we can leverage economies of scale from standard LED manufacturers and simplify assembly. Physics: This relies on standard LED lumen output and beam pattern characteristics being sufficient for automotive signaling regulations (ECE R37, FMVSS 108). Validation will involve photometric testing to ensure compliance with intensity, color, and angular distribution requirements for each function. Durability testing (vibration, thermal cycling, ingress protection) will be crucial for the modular components and their interconnections. Cost analysis will focus on Bill of Materials (BOM) reduction and assembly time optimization. | 0 | AI Proposal | The current integrated LED tail lamp module likely involves complex custom PCB design and specialized LED integration, driving up tooling and per-unit costs. By adopting a modular approach, we can leverage economies of scale from standard LED manufacturers and simplify assembly. Physics: This relies on standard LED lumen output and beam pattern characteristics being sufficient for automotive signaling regulations (ECE R37, FMVSS 108). Validation will involve photometric testing to ensure compliance with intensity, color, and angular distribution requirements for each function. Durability testing (vibration, thermal cycling, ingress protection) will be crucial for the modular components and their interconnections. Cost analysis will focus on Bill of Materials (BOM) reduction and assembly time optimization. | VAVE | TBD
AI-GEN-02 | Substitute the current multi-piece polycarbonate tail lamp lens with a single, injection-molded clear polycarbonate lens with integrated light pipes or diffusion layers for red and amber illumination, eliminating the need for separate colored lenses and associated assembly steps. | The existing tail lamp likely uses multiple colored polycarbonate lenses or films, requiring precise alignment and bonding. A single-piece lens with internal light management can simplify manufacturing and reduce part count. Physics: This leverages the optical properties of polycarbonate and the principles of total internal reflection and diffusion. Light pipes will guide illumination from a common white LED source to the desired red or amber output regions. Validation requires optical simulation to ensure uniform light distribution and color purity across the lens surface. Photometric testing of the final assembly against regulatory standards is essential. Material characterization of the polycarbonate for UV resistance and impact strength will also be performed. | 0 | AI Proposal | The existing tail lamp likely uses multiple colored polycarbonate lenses or films, requiring precise alignment and bonding. A single-piece lens with internal light management can simplify manufacturing and reduce part count. Physics: This leverages the optical properties of polycarbonate and the principles of total internal reflection and diffusion. Light pipes will guide illumination from a common white LED source to the desired red or amber output regions. Validation requires optical simulation to ensure uniform light distribution and color purity across the lens surface. Photometric testing of the final assembly against regulatory standards is essential. Material characterization of the polycarbonate for UV resistance and impact strength will also be performed. | VAVE | TBD
AI-GEN-03 | Re-evaluate the tail lamp housing material from the current high-performance plastic (e.g., ABS/PC blend) to a more cost-effective, yet structurally sound, filled polypropylene (PP) or talc-filled PP, provided it meets thermal and impact requirements. | High-performance plastics often carry a premium. Exploring filled polypropylenes can offer significant material cost savings without compromising essential mechanical properties for tail lamp housings. Physics: The primary function of the housing is structural support and environmental sealing. Filled PP offers good stiffness and dimensional stability, while talc-fill can further enhance these properties and reduce shrinkage. Validation will involve material property testing (tensile strength, flexural modulus, impact resistance - Izod/Charpy) to ensure it meets the design specifications. Thermal stability testing (heat deflection temperature) and UV aging tests will be critical. FEA simulations will be used to confirm structural integrity under load and vibration. | 0 | AI Proposal | High-performance plastics often carry a premium. Exploring filled polypropylenes can offer significant material cost savings without compromising essential mechanical properties for tail lamp housings. Physics: The primary function of the housing is structural support and environmental sealing. Filled PP offers good stiffness and dimensional stability, while talc-fill can further enhance these properties and reduce shrinkage. Validation will involve material property testing (tensile strength, flexural modulus, impact resistance - Izod/Charpy) to ensure it meets the design specifications. Thermal stability testing (heat deflection temperature) and UV aging tests will be critical. FEA simulations will be used to confirm structural integrity under load and vibration. | VAVE | TBD
AI-GEN-04 | Simplify the tail lamp electrical connector by moving from a multi-pin, sealed connector to a simpler, fewer-pin connector or a direct wire-to-board connection with appropriate sealing and strain relief, assuming the signal complexity allows. | Complex connectors add cost through the connector housing, pins, and assembly labor. Simplification can lead to direct savings. Physics: This relies on the ability to consolidate electrical functions into fewer pins or eliminate them entirely if direct connections are feasible. The fundamental principle is ensuring reliable electrical contact and environmental protection. Validation will involve testing the simplified connection for electrical continuity, vibration resistance, and ingress protection (IP rating) against the required automotive standards. Current carrying capacity and voltage drop across the connection will also be verified. | 0 | AI Proposal | Complex connectors add cost through the connector housing, pins, and assembly labor. Simplification can lead to direct savings. Physics: This relies on the ability to consolidate electrical functions into fewer pins or eliminate them entirely if direct connections are feasible. The fundamental principle is ensuring reliable electrical contact and environmental protection. Validation will involve testing the simplified connection for electrical continuity, vibration resistance, and ingress protection (IP rating) against the required automotive standards. Current carrying capacity and voltage drop across the connection will also be verified. | VAVE | TBD
AI-GEN-05 | Eliminate the dedicated light guide for the rear fog lamp if its functionality can be integrated into the main brake light illumination or a secondary brake light, provided regulatory compliance can still be met by the combined illumination. | A dedicated light guide for a single-function lamp adds complexity and cost. Integrating this function into existing illuminated areas simplifies the design. Physics: This hinges on the ability to achieve the required intensity and visibility for the rear fog lamp function from an already illuminated component (e.g., brake light) without compromising its primary function or violating regulations. Validation will involve photometric measurements of the combined illumination to ensure the rear fog lamp meets its specific intensity and visibility requirements, especially in adverse weather conditions. Regulatory review for compliance with UN ECE R38 or equivalent standards is paramount. | 0 | AI Proposal | A dedicated light guide for a single-function lamp adds complexity and cost. Integrating this function into existing illuminated areas simplifies the design. Physics: This hinges on the ability to achieve the required intensity and visibility for the rear fog lamp function from an already illuminated component (e.g., brake light) without compromising its primary function or violating regulations. Validation will involve photometric measurements of the combined illumination to ensure the rear fog lamp meets its specific intensity and visibility requirements, especially in adverse weather conditions. Regulatory review for compliance with UN ECE R38 or equivalent standards is paramount. | VAVE | TBD
Generated by VAVE-AI

## Slide 4
Ideas Summary (Part 3)
Idea ID | Proposal | Imp | Saving Value | Status | Way Forward | Responsibility | Date
AI-GEN-06 | Consolidate the tail lamp control logic into the Body Control Module (BCM) or a dedicated micro-controller within the vehicle's existing network, rather than using a separate, dedicated controller within the tail lamp assembly, if current complexity allows. | Dedicated controllers within lighting modules add cost and complexity. Centralizing control within the vehicle's main ECUs leverages existing infrastructure. Physics: This relies on the vehicle's network (CAN, LIN) having sufficient bandwidth and processing power to handle the tail lamp control signals. The principle is to reduce distributed intelligence and associated hardware. Validation will involve communication protocol testing to ensure reliable data exchange between the BCM and the tail lamps. Functional testing of all tail lamp operations (parking lights, brake lights, turn signals, reverse lights, fog lights) controlled by the BCM will be performed. Electromagnetic compatibility (EMC) testing of the integrated system is crucial. | 0 | AI Proposal | Dedicated controllers within lighting modules add cost and complexity. Centralizing control within the vehicle's main ECUs leverages existing infrastructure. Physics: This relies on the vehicle's network (CAN, LIN) having sufficient bandwidth and processing power to handle the tail lamp control signals. The principle is to reduce distributed intelligence and associated hardware. Validation will involve communication protocol testing to ensure reliable data exchange between the BCM and the tail lamps. Functional testing of all tail lamp operations (parking lights, brake lights, turn signals, reverse lights, fog lights) controlled by the BCM will be performed. Electromagnetic compatibility (EMC) testing of the integrated system is crucial. | VAVE | TBD
WEB-GEN-01 | Streamline Design and Technical Team Collaboration | Implement cross-functional workshops and integrated project management tools to foster better communication and alignment between design and technical engineering teams. This can reduce rework and accelerate development cycles, leading to cost savings. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | 0 | Web Sourced | Implement cross-functional workshops and integrated project management tools to foster better communication and alignment between design and technical engineering teams. This can reduce rework and accelerate development cycles, leading to cost savings. Source: https://www.f1technical.net/forum/viewtopic.php?t=32104&start=90 | VAVE | TBD
WEB-GEN-02 | Optimize Aerodynamic Configurations for Specific Tracks | Conduct detailed CFD analysis and wind tunnel testing to identify and implement aerodynamic packages that are optimized for low downforce circuits (e.g., Monza, Baku, Vegas). This can involve designing specific wing elements or bodywork modifications that reduce drag and improve straight-line speed, potentially reducing the need for excessively powerful and costly engine configurations. Source: https://www.f1technical.net/forum/viewtopic.php?t=32054&start=8220 | 0 | Web Sourced | Conduct detailed CFD analysis and wind tunnel testing to identify and implement aerodynamic packages that are optimized for low downforce circuits (e.g., Monza, Baku, Vegas). This can involve designing specific wing elements or bodywork modifications that reduce drag and improve straight-line speed, potentially reducing the need for excessively powerful and costly engine configurations. Source: https://www.f1technical.net/forum/viewtopic.php?t=32054&start=8220 | VAVE | TBD
Generated by VAVE-AI

## Slide 5: Chart Analysis Discussion
Chart: Cost Savings by Idea
| 2311-EL-ID-18 | 2311-EL-ID-06 | 2311-IT-ID-19 | 2311-PRODUCT-ID-24 | 2311-PRODUCT-ID-01 | AI-GEN-01 | AI-GEN-02 | AI-GEN-03 | AI-GEN-04 | AI-GEN-05 | AI-GEN-06 | WEB-GEN-01 | WEB-GEN-02
Savings (INR) | 42 | 126 | 56 | 64 | 68 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Generated by VAVE-AI

## Slide 6: Pie chart for ideas status
Chart: Ideas Status Distribution
| Implemented | Status OK | Status TBD | Status NG
Status | 0 | 0 | 1 | 3
• Total Ideas: 13
• Total Potential Savings: INR 356.00
• Implemented Ideas: 0
• Status OK: 0
• Status TBD: 1
• Status NG: 3
• The provided cost reduction ideas focus on process deletions and material replacements to reduce manufacturing costs.
• Key proposals include removing paint coatings from brackets and mounts, replacing PC-ABS with ABS, and switching to galvanized steel for window regulators.
• These changes aim to maintain functionality while reducing costs and, in some cases, weight.
Generated by VAVE-AI

## Slide 7: Summary section
Total Ideas: 13 ideas analyzed.
Total Savings: INR 356.00 in potential cost reductions.
Key Proposals: Remove paint coatings from mounts and brackets, replace PC-ABS with ABS, and use galvanized steel for window regulators.
Status: All ideas currently TBD, pending further evaluation.
Focus: Cost reduction through process deletion and material substitution while maintaining functionality.
Generated by VAVE-AI